## Slide 1
Constructive Computer Architecture:
Basics of Branch Prediction
Thomas Bourgeat - EPFL
Slides prepared with Arvind
Electrical Engineering and Computer Science
Massachusetts Institute of Technology

## Slide 2: Control Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
  Number of instructions in pipelined
What fraction of executed instructions are branch instructions?
Which instructions change the control flow?

## Slide 3: How frequent are branches? ARM Cortex 7
Blem et al [HPCA 2013] Spec INT 2006
 | ARM Cortex-A9; ARMv7 ISA |  |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
astar | 1.47E+10 | 16.0 | 55.6 | 13.0 | 15.4
bzip2 | 2.41E+10 | 8.7 | 34.6 | 14.4 | 42.2
gcc | 5.61E+09 | 10.2 | 19.1 | 11.2 | 59.5
gobmk | 5.75E+10 | 10.7 | 25.4 | 7.2 | 56.8
hmmer | 1.56E+10 | 5.1 | 41.8 | 18.1 | 35.0
h264 | 1.06E+11 | 5.5 | 30.4 | 10.4 | 53.6
libquantum | 3.97E+08 | 11.5 | 8.1 | 11.7 | 68.7
omnetpp | 2.67E+09 | 11.7 | 19.3 | 8.9 | 60.1
perlbench | 2.69E+09 | 10.7 | 24.6 | 9.3 | 55.5
sjeng | 1.34E+10 | 11.5 | 39.3 | 13.7 | 35.5
Average |  | 8.2 | 31.9 | 10.9 | 49.0
Every 12th instruction is a branch

## Slide 4: How frequent are branches? X86
 |  | core i7; x86 ISA |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
astar | 5.71E+10 | 6.9 | 19.5 | 6.9 | 66.7
bzip2 | 4.25E+10 | 11.1 | 31.2 | 11.8 | 45.9
hmmer | 2.57E+10 | 5.3 | 30.5 | 9.4 | 54.8
gcc | 6.29E+09 | 15.1 | 22.1 | 14.1 | 48.7
gobmk | 8.93E+10 | 12.1 | 21.7 | 13.4 | 52.7
h264 | 1.09E+11 | 7.1 | 46.8 | 18.5 | 27.6
libquantum | 4.18E+08 | 13.2 | 39.3 | 6.8 | 40.7
omnetpp | 2.55E+09 | 16.4 | 28.6 | 21.4 | 33.7
perlbench | 2.91E+09 | 17.3 | 25.9 | 16.0 | 40.8
sjeng | 2.11E+10 | 14.8 | 22.8 | 11.0 | 51.4
Average |  | 9.4 | 31.0 | 13.4 | 46.2
Blem et al [HPCA 2013] Spec INT 2006
Every 10th or 11th instruction is a branch

## Slide 5: How frequent are branches? ARM Cortex 7
Blem et al [HPCA 2013] Spec FP 2006
 | ARM Cortex-A9; ARMv7 ISA |  |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
bwaves | 3.84E+11 | 13.5 | 1.4 | 0.5 | 84.7
cactusADM | 1.02E+10 | 0.5 | 51.4 | 17.9 | 30.1
leslie3D | 4.92E+10 | 6.2 | 2.0 | 3.7 | 88.1
milc | 1.38E+10 | 6.5 | 38.2 | 13.3 | 42.0
tonto | 1.30E+10 | 10.0 | 40.5 | 14.1 | 35.4
Average |  | 12.15 | 4.68 | 1.95 | 81.22
Every 8th instruction is a branch

## Slide 6: How frequent are branches? X86
Blem et al [HPCA 2013] Spec FP 2006
 |  | core i7; x86 ISA |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
bwaves | 3.41E+10 | 3.2 | 51.4 | 16.8 | 28.7
cactusADM | 1.05E+10 | 0.4 | 55.3 | 18.6 | 25.8
leslie3D | 6.25E+10 | 4.9 | 35.3 | 12.8 | 46.9
milc | 3.29E+10 | 2.2 | 32.2 | 13.8 | 51.8
tonto | 4.88E+09 | 7.1 | 27.2 | 12.4 | 53.3
Average |  | 3.6 | 39.6 | 14.4 | 42.4
Every 27th instruction is a branch

## Slide 7: Observations
Control transfer happens every 8th to 30th instruction
Static vs dynamic predictors: Does the prediction depend upon the execution history?
Processors often use more than one predictor
  Need a method to integrate multiple prediction schemes in the pipeline
  Understand the interactions and the performance implications of various predictors
There is a plethora of branch prediction schemes – their importance grows with the depth of processor pipeline
we will start with the basics ...

## Slide 8: RISC V Branches & Jumps
Instruction Direction known after Target known after
JAL
JALR
BEQ/BNE ...
Each instruction fetch depends on some information from the preceding instruction:
1. Is the preceding instruction a taken branch?
2. If so, what is the target address?
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Reg. Fetch
After Exec
A predictor can redirect the pc only after the relevant information required by the predictor is available

## Slide 9: Overview of control prediction
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Given (pc, ppc), a misprediction can be corrected (used to redirect the pc) as soon as it is detected. In fact, pc can be redirected as soon as we have a “better” prediction.
mispred insts must be filtered
correct mispred
correct mispred
correct mispred
This redirection is not a prediction
Notes: Notice – all instructions in the pipeline are predictions except for the ones whose PC was set by the Redirection. The instruction whose PC was set by Redirection always has a new epoch associated with it. Such an instruction can not be killed. However, one can kill any predicted instruction and make a better prediction.

## Slide 10: Static Branch Prediction
Since most instructions do not result in a control transfer, pc+4 is a good predictor
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64
  reported as ~80% accurate
JZ
JZ
backward
90%
forward
50%
... but our ISA is fixed!

## Slide 11: Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)
pc
Truth/Feedback
Prediction
Predictor
update
predict

## Slide 12: Next Address Predictor: Branch Target Buffer (BTB)
BTB permits ppc to be determined before the instruction is decoded
iMem
pc
tag(pci)
targeti
valid
match
k
2k-entry direct-mapped BTB
BTB remembers recent target PCs for a set of control instructions
  Fetch: looks for the pc and the associated target in BTB; if pc is not found then ppc is pc+4
  Execute: checks prediction, if wrong poisons the wrong-path instructions; updates the BTB for jumps and taken-branches
Even small BTBs are very effective
Zero-size BTB behaves like the pc+4 nap
BTB area can be reduced by making tags arbitrarily small!

## Slide 13: Next Addr Predictor interface
interface AddrPred; method Addr nap(Addr pc); method Action update(Addr pc, Addr nextPC,
Bool taken); endinterface
Predictor training: On a pc misprediction, pc and epoch are updated, and the relevant information is passed to the next address predictor
  nap: simple look up
  update: On a pc misprediction, if the jump or branch at the pc was taken then the BTB is updated with the new (pc, nextPC) otherwise the pc entry is deleted

## Slide 14: BTB predictor update method
method Action update(Addr pc, Addr nextPC,
Bool taken);
extract index and tag from pc; if (branch taken) then update BTB with the new prediction;
mark the entry pc as branch taken;
else mark the entry pc as branch not taken endmethod

## Slide 15: Integrating BTB in the 4-Stage pipeline
...
AddrPred btb <- mkBtb
rule fetch; iMem.enq(pc[1]);
let ppcF = nap(pc[1]); pc[1] <= ppcF;
f2d.enq(Fetch2Decode(pc:pc[1], ppc:ppcF,
epoch:epoch[1]));
endrule rule decode; ...//no change
rule execute; ...
rule writeBack; ... //no change
btb.nap(pc[1])

## Slide 16: 4-Stage-pipeline without Branch predictors execute stage
rule execute; let x = d2e.first; ...
if(epoch is wrong) begin e2w.enq(Invalid); d2e.deq; end
else
execute the instruction;
Initiate memory request if it’s a memory instruction;
if (prediction (ppc) is wrong) then update the pc, epoch and
e2w.enq(Valid Exec12Exec2(eInst:eInst, pc:pcE));
d2e.deq;
endrule
for btb training, btb.update(pcE, nextPC, eInst.brTaken);

## Slide 17: Multiple Predictors: BTB + Branch Direction Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Wrong path inst must be filtered
Br Dir Pred
correct mispred
correct mispred

## Slide 18: Branch Prediction Bits Remember how the branch was resolved previously
Assume 2 BP bits per instruction
Use saturating counter
On ¬taken  |  On taken | 1 | 1 | Strongly taken
 |  | 1 | 0 | Weakly taken
 |  | 0 | 1 | Weakly ¬taken
 |  | 0 | 0 | Strongly ¬taken
Direction prediction changes only after two successive bad predictions

## Slide 19: Two-bit versus one-bit Branch prediction
Consider the branch instruction needed to implement a loop
  with one bit, the prediction will always be set incorrectly on loop exit
  with two bits the prediction will not change on loop exit
A little bit of hysteresis is good in changing predictions

## Slide 20: Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct direction predictions
0
0
Fetch PC
Branch?
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?
Target PC
+
After decoding
At the Decode stage:
For a branch instruction consult the BHT to determine the direction prediction;
Use the prediction to compute the nextPC;
If the nextPC is different from the incoming ppc, redirect the Fetch
No need to keep the target PC because it can be computed

## Slide 21: Where does BHT fit in the processor pipeline?
BHT can only be used after instruction decode
We still need the next instruction address predictor (e.g., BTB) at the fetch stage
Predictor training: On a pc misprediction, information about redirecting the pc has to be passed to the fetch stage. However, for training the direction predictor, the direction information has to be passed after every branch execution (misprediction or not)

## Slide 22: Multiple predictors in a pipeline
At each stage we need to take two decisions:
  Determine if the current instruction is a wrong path instruction: Requires looking at epochs
  Determine if the prediction (ppc) following the current instruction is good: Requires consulting BTB at Decode, and later determining the actual branch resolution at Execute
No redirections should be generated by known wrong path instructions
Redirections from Execute stage are always correct, and cannot be ignored
  Should training also be avoided by wrong path instruction?
  Generally yes, but may have some benefits

## Slide 23: N-Stage pipeline with BHT
Both Decode and Execute can redirect the PC; Execute redirect should never be overruled
Use separate epochs for each redirecting stage
  eEp for Execute redirections and dEp for Decode redirections
Execute can update both BTB and BHT
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
redirect PC
dEp
...
eEp
BTB
BHT
{pc,ppc,ieEp,...}
{pc,ppc,ieEp,idEp,...}
{pc, newPc, taken}
{pc, newPc}

## Slide 24: N-Stage pipeline with BHT Decode stage branch prediction activity
Is ieEp = eEP ?
Is idEp = dEp ?
yes
no
yes
no
Current instruction is OK; Consult BHT for branches
Wrong path instruction; drop it
increment dEp; redirect
Wrong path instruction; drop it
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
dEp
...
eEp
BTB
BHT
{pc,ppc,ieEp,...}
{pc,ppc,ieEp,idEp,...}
{pc, newPc, taken}
{pc, newPc,}
!misprediction
misprediction
No action

## Slide 25: A small problem
Consider the entry in BTB for a branch at the end of a loop
  Execute will delete it on loop exit
  This will cause a misprediction when the loop is executed again!
  Decode will redirect again after consulting BHT!
How to prevent Execute from deleting the entry?

## Slide 26: Possible Fixes
Execute could read the BHT entry and not delete the entry from BTB
  To avoid reading the BHT from two places, the direction prediction bits could be passed from the Decode to Execute
We can keep the history bits for branches in the BTB also and update as necessary;
We can set the branches to be always-taken

## Slide 27: Discussion
The number of entries in BTB is small both because of the need for fast access and the need to store the target address (small and fat)
The number entries in BHT is large (thin and tall)
Jumps through registers (JALR) are problematic and perhaps should not be kept in the BTB

## Slide 28: Uses of Jump Register (JALR)
(Dynamic) function call (jump to (run-time) function address)
Subroutine returns (jump to return address)
How can we improve subroutine call transfers?
BTB will work well only if the same function is called repeatedly
BTB is not likely to work because a function is called from many distinct call sites!

## Slide 29: Return Address Stack
Maintain RAS, a small structure which holds pcs to accelerate JR for subroutine returns
pc of fb call
pc of fc call
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
pc of fd call
k entries
(typically k=8-16)
Pop return address when subroutine return decoded
Push call address when function call executed
Don’t enter these instructions in BTB
RAS

## Slide 30: Multiple Predictors: BTB + BHT + Ret Predictors
The system must work even if every prediction is wrong
Multiple predictors are common;
Performance analysis is quite difficult – depends upon the sizes of various tables and program behavior
In superscalar architectures the branch prediction problem changes to the cache-line prediction problem
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Wrong path insts must be filtered
Br Dir Pred, RAS
correct
JR pred
correct mispred

## Slide 31: Takeaway
Branch-prediction has first order effect on the performance of your machine
There are just too many branch prediction schemes to be covered in class but the three discussed here – BTB, BHT and RAS – will take you very far
The exact choice depends upon the other features of the microarchitecture as well

## Slide 32: More advanced direction prediction

## Slide 33: Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor and the predictor uses this information to predict the resolution of the next branch
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition is false, then so is second condition

## Slide 34: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Taken/¬Taken?
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register h
Four
2k, 2-bit
Entry
BHT

## Slide 35: Outlining TAGE predictor http://www.irisa.fr/caps/people/seznec/JILP-COTTAGE.pdf

## Slide 36: Insights
"Prediction" is a bit misleading
  We are just remembering the past!
Branches predictors:
  Identify branch (pc)
  Identify context (history)
  This is enough to predict most branches
Some branches are unpredictable

## Slide 37: Generalizing Predictions
Prediction is not only about branches
  Pc + 4 for ALU instruction is a prediction !
  JALR need "predictions" too !
Prediction is not even only about control flow!
  Predicting the size of instructions
  Predicting address aliasing

## Slide 38: Thanks!

## Slide 39: 4-Stage-pipeline without Branch predictors fetch, decode
rule fetch; iMem.enq(pc[1]);
let ppcF = nap(pc[1]); pc[1] <= ppcF ;
f2d.enq(Fetch2Decode(pc:pc[1], ppc:ppcF, epoch:epoch[1]))
endrule
rule decode;
let inst = iMem.first; let x = f2d.first;
if(epoch[1] != x.inEp) begin iMem.deq; f2d.deq end //wrongpath
else begin
let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin …fetch register values d2e.enq(Decode2Execute{pc: x.pc, ppc: x.ppc,
dIinst: dInst, epoch: x.epoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); iMem.deq; f2d.deq end endrule

## Slide 40: 4-Stage-pipeline without Branch predictors execute
rule execute; let x = d2e.first; ...
if(epoch[0] != inEp) begin e2w.enq(Invalid); d2e.deq; end
else begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE);
if(eInst.iType == Ld)
dMem.enq(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) begin
dMem.enq(MemReq{op:St, addr:eInst.addr,
data:eInst.data}); end
let nextPC = eInst.brTaken ? eInst.addr : pcE + 4;
if (x.ppc != nextPC) begin pc[0] <= eInst.addr;
epoch[0] <= !epoch[0]; end
e2w.enq(Valid Exec12Exec2(eInst:eInst, pc:pcE));
d2e.deq;
end
endrule

## Slide 41: 4-Stage-pipeline without Branch predictors writeback
rule writeback;
let vx = e2w.first;
if (vx matches tagged Valid .x) begin
let pcE=x.pc; let eInst=x.eInst;
if (isValid(eInst.dst)) begin
let data = eInst.iType==Ld ? dMem.first: eInst.data;
rf.wr(fromMaybe(?, eInst.dst), data);
end
if(eInst.iType == Ld) dMem.deq;
end
sb.remove; e2w.deq; endrule

## Slide 42: BTB predictor
module mkBtb(AddrPred); RegFile#(BtbIndex, Addr) ppcArr <- mkRegFileFull; RegFile#(BtbIndex, BtbTag) entryPcArr <- mkRegFileFull; Vector#(BtbEntries, Reg#(Bool))
validArr <- replicateM(mkReg(False));
function BtbIndex getIndex(Addr pc)=truncate(pc>>2); function BtbTag getTag(Addr pc) = truncateLSB(pc);
method Addr nap(Addr pc); BtbIndex index = getIndex(pc); BtbTag tag = getTag(pc); if(validArr[index] && tag == entryPcArr.sub(index)) return ppcArr.sub(index); else return (pc + 4); endmethod
method Action update(Addr pc, Addr nextPC, Bool taken);…
endmodule

## Slide 43: 4-Stage-pipeline with BTB fetch, decode
rule fetch; iMem.enq(pc[1]);
let ppcF = btb.nap(pc[1]); pc[1] <= ppcF ;
f2d.enq(Fetch2Decode(pc:pc[1], ppc:ppcF, epoch:epoch[1]))
endrule
rule decode;
let inst = iMem.first; let x = f2d.first;
if(epoch[1] != x.inEp) begin iMem.deq; f2d.deq end //wrongpath
else begin
let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin …fetch register values d2e.enq(Decode2Execute{pc: x.pc, ppc: x.ppc,
dIinst: dInst, epoch: x.epoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); iMem.deq; f2d.deq end endrule

## Slide 44: 4-Stage-pipeline with BTB execute
rule execute; let x = d2e.first; ...
if(epoch[0] != inEp) begin e2w.enq(Invalid); d2e.deq; end
else begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE);
if(eInst.iType == Ld)
dMem.enq(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) begin
dMem.enq(MemReq{op:St, addr:eInst.addr,
data:eInst.data}); end
let nextPC = eInst.brTaken ? eInst.addr : pcE + 4;
if (x.ppc != nextPC) begin pc[0] <= eInst.addr;
epoch[0] <= !epoch[0];
btb.update(pcE, nextPC, eInst.brTaken); end
e2w.enq(Valid Exec12Exec2(eInst:eInst, pc:pcE));
d2e.deq; end
endrule

## Slide 45: 4-Stage-pipeline with BTB writeback
rule writeback;
let vx = e2w.first;
if (vx matches tagged Valid .x) begin
let pcE=x.pc; let eInst=x.eInst;
if (isValid(eInst.dst)) begin
let data = eInst.iType==Ld ? dMem.first: eInst.data;
rf.wr(fromMaybe(?, eInst.dst), data);
end
if(eInst.iType == Ld) dMem.deq;
end
sb.remove; e2w.deq; endrule

## Slide 47: Direction Predictor interface
interface DirectionPred; method Addr ppcDP(Addr pc, Addr targetPC); method Action update(Addr pc, Bool taken); endinterface

## Slide 48: BHT predictor
module mkBHT(DirectionPred); Vector#(BhtEntries, Reg#(Bit#(2)))
bhtArr <- replicateM(mkReg(2’b01));
function BhtIndex getBhtIndex(Addr pc)= ...;
function Addr computeTarget(Addr pc, Addr targetPC,
Bool taken)= ...; define functions extractDir; getBhtEntry, newDpBits; ...
method Addr ppcDP(Addr pc, Addr targetPC); BtbIndex index = getBhtIndex(pc);
let direction = extractDir(bhtArr[index]); return computeTarget(pc, targetPC, direction); endmethod
method Action update(Addr pc, Bool taken);
BtbIndex index = getBhtIndex(pc);
let dpBits = getBhtEntry(index);
bhtArr[index] <= newDpBits(dpBits,taken); endmethod
endmodule

## Slide 49: 4-Stage-pipeline with BTB and BHT fetch
rule fetch; iMem.enq(pc[1]);
let ppcF = btb.nap(pc[1]); pc[1] <= ppcF ;
f2d.enq(Fetch2Decode{pc:pc[1], ppc:ppcF, eEp:eEp[1],
dEp:dEp[1]});
endrule

## Slide 50: 4-Stage-pipeline with BTB and BHT decode
rule decode;
let inst = iMem.first; let x = f2d.first;
let pcD=x.pc; let ppcD=x.ppc; let ieEp=x.eEp; let idEp=x.dEp;
if (eEp[1] != ieEp) begin iMem.deq; f2d.deq; end //wrong-path
else begin
if (dEp[0] != idEp) begin iMem.deq; f2d.deq; end //wrong-path
else begin //right-path instruction
let dInst = decode(inst);
let stall = ...; // normal execution
if(!stall) begin
let ppcDP = isBranch(dInst)? bht.ppcDP(pcD,dInst.add) : ppcD;
if (ppcDP!= ppcD) begin dEp[0]<= !dEp[0]; pc[1]<= ppcDP; end …fetch register values d2e.enq(Decode2Execute{ pc: pcD, ppc: ppcDP, eEp: ieEp,
dIinst: dInst, rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); iMem.deq; f2d.deq end end
endrule

## Slide 51: 4-Stage-pipeline with BTB and BHT execute
rule execute; let x = d2e.first; ...
if(eEp[0] != inEp) begin e2w.enq(Invalid); d2e.deq; end
else begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE);
if(eInst.iType == Ld)
dMem.enq(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) begin
dMem.enq(MemReq{op:St, addr:eInst.addr,
data:eInst.data}); end
let nextPC = eInst.brTaken ? eInst.addr : pcE + 4;
if (x.ppc != nextPC) begin pc[0] <= eInst.addr;
epoch[0] <= !epoch[0];
btb.update(pcE, nextPC, eInst.brTaken); end
if (isBranch(dInstE)) bht.update(pcE, eInst.brTaken);
e2w.enq(Valid Exec12Exec2{eInst:eInst, pc:pcE});
d2e.deq; end
endrule

## Slide 52: 4-Stage-pipeline with BTB and BHT writeback
rule writeBack;
let vx = e2w.first;
if (vx matches tagged Valid .x) begin
let pcE=x.pc; let eInst=x.eInst;
if (isValid(eInst.dst)) begin
let data = eInst.iType==Ld ? dMem.first: eInst.data;
rf.wr(fromMaybe(?, eInst.dst), data);
end
if(eInst.iType == Ld) dMem.deq;
end
sb.remove; endrule