## Slide 1
Constructive Computer Architecture:
Multirule systems and Concurrent Execution of Rules
Prepared by Arvind
Electrical Engineering and Computer Science
Massachusetts Institute of Technology

## Slide 2: Plan for the day
Module 1: The different kind of memories
Module 2: Systems with multiple rules
Module 3: Scheduling circuitry

## Slide 3
First, we will examine some storage elements and then study the concurrency issue

## Slide 4: Register File 2 Read ports + 1 Write port
typedef Bit#(32) Word;
typedef Bit#(5) RIndx;
interface RFile2R1W;
method Word rd1(RIndx index) ;
method Word rd2(RIndx index) ;
method Action wr (RIndx index, Word data);
endinterface
Registers can be read or written any time, so the guards are always true (not shown)
rd1
rf
rd2
wr
en
data
index
data
index
data
index

## Slide 5: Register File - usage Reads are combinational
// rf was declared as a register file
rule example_use_rf;
Bit#(32) v1 = rf.rd1(0x1); // read value in register 1
Bit#(32) v2 = rf.rd2(0x10); // read value in register 16
rf.wr(0x11, v1+v2); // write the sum in register 17
endrule
rd1
rf
rd2
wr
en
data
index
data
index
data
index
rule nonexample; // DOES NOT WORK​
rf.wr(0x11, 1); // write 1 in register 17?​
rf.wr(0x12, 2); // write 2 in register 18?​
endrule

## Slide 6: Magic Memory
Reads and Writes behave as in a register file (not true for real SRAM or DRAM)
  Reads are combinational
  Write, if enabled, is performed at the rising clock edge
However, unlike a register file, there is only one port/method, which is used either for reading or for writing
MAGIC
RAM
ReadData
WriteData
Address
WriteEnable
Clock

## Slide 7: Magic Memory Interface
interface MagicMemory;
method ActionValue#(Word) req(MemReq r);
endinterface
typedef struct {MemOp op; Word addr; Word data;}
MemReq deriving(Bits, Eq);
typedef enum {Ld, St} MemOp deriving(Bits, Eq);
Magic memory can be read or written any time, so the guards are always true (not shown)
memReq
magic memory
load data
op
address
store data
en
let data <- m.req(MemReq{op:Ld, addr:a, data:?});
let dummy <- m.req(MemReq{op:St, addr:a, data:v});
Usage:

## Slide 8: SRAMs and BRAMs (memory on FPGAs)
A read takes more than one cycle – therefore, a read is performed in two phases:
  A read request is sent
  After one or more cycles a response comes back
A write generates a response only if the write request asks for a response
Reading a response and sending a new request can be performed in the same cycle

## Slide 9: BRAM Interface – 1 port
interface BRAM1Port;
interface PORTIFC portA;
endinterface
interface PORTIFC;
interface Put request;
interface Get response;
endinterface
portA
BRAM
Response
interface Put;
method Action
put(BRAMRequest);
endinterface
interface Get;
method ActionValue#(DATA)
get();
endinterface
Request
Interface PORTIFC consists of two sub-interfaces Put and Get

## Slide 10: BRAM Interface – 2 port
interface BRAM2Port;
interface PORTIFC portA;
interface PORTIFC portB;
endinterface
BRAM
portA
BRAM
Response
Request
portA
Response
Request

## Slide 11: BRAM: read/write request
Instantiation
BRAM1Port#(AddrType, Data) mem <-
mkBRAM1Server(defaultValue);
Read request
mem.portA.request.put(BRAMReq{write:False, responseOnWrite:False, address:addr, datain:?})
Write request
mem.portA.request.put(BRAMReq{write:True, responseOnWrite:False, address:addr, datain:val})
Read response
let x <- mem.portA.response.get();

## Slide 12: Summary: memory and their interfaces
Register file and "Magic memory"
BRAM (1 or 2 ports)
One more in labs/recitation: vector of registers

## Slide 13: Systems with multiple rules

## Slide 14: A one-instruction vector machine
Adds k to each element of an n-element vector a and store it in b
Vectors are too large to be stored in registers and therefore stored in BRAM
BRAM interface is single ported
Let a and b be the current pointers to the vectors, and n be the number of elements in the vector that remain to be processed
BRAM
a
b
a
b
+k
n
Let us build such a machine

## Slide 15: Steps in processing
Assume a, b, n and BRAM have been initialized properly
Initiate a BRAM request to read an element of a; increment a
Wait for the result; add k;
initiate a write of the result in b; increment b; decrement n
Repeat these steps if n>0
BRAM
a
b
a
b
+k
n
Let a and b be the current pointers to the vectors, and n be the number of elements in the vector that remain to be processed

## Slide 16: Rules for the vector machine
rule init_read_a if (n>0 && turn == 0);
mem.portA.request.put(BRAMReq{write:False,writeRes:False,
address:a, datain:?});
a <= a + 1;
n <= n – 1;
turn <= 1;
endrule
rule read_result if (turn == 1);
let x <- mem.portA.response.get();
mem.portA.request.put(BRAMReq{write:True, writeRes:False,
address:b, datain:x + k});
b <= b + 1;
turn <= 0;
endrule

## Slide 17: Multi-rule Systems
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
One-rule-at-a-time-semantics: Any legal behavior of a Bluespec program can be explained by observing the state updates obtained by applying only one rule at a time
Non-deterministic choice; User annotations can be used in rule selection
However, for performance we execute multiple rules concurrently whenever possible

## Slide 18: Rules for the vector machine
rule init_read_a if (n>0 && turn == 0);
mem.portA.request.put(BRAMReq{write:False,writeRes:False,
address:a, datain:?});
a <= a + 1;
n <= n – 1;
turn <= 1;
endrule
rule read_result if (turn == 1);
let x <- mem.portA.response.get();
mem.portA.request.put(BRAMReq{write:True, writeRes:False,
address:b, datain:x + k});
b <= b + 1;
turn <= 0;
endrule
The design still works without taking turn! Or does it?

## Slide 19: Homework
To get familiarized with this programming/execution model:
  Lab1-b: debug a simple multi-rule machine that fail to compute dot products
  Lab2: write your own matrix/matrix multiply module

## Slide 20: Multi-rule systems and concurrency

## Slide 21: Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1;
fifo1.enq(f1(inQ.first));
inQ.deq(); endrule
rule stage2;
fifo2.enq(f2(fifo1.first));
fifo1.deq; endrule
rule stage3;
outQ.enq(f3(fifo2.first));
fifo2.deq; endrule
Can these rules fire concurrently?
Yes, but it must be possible to do enq and deq on a fifo
simultaneously

## Slide 22: One-Element FIFO Implementation
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
Can enq and deq methods be ready at the same time?
No! Therefore, they cannot execute concurrently!

## Slide 23: Concurrency when the FIFOs do not permit concurrent enq and deq
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
not empty
not empty
&
not full
not empty
&
not full
not full
At best alternate stages in the pipeline will be able to fire concurrently

## Slide 24: Two-Element FIFO
Initially, both va and vb are false
First enq will store the data in da and mark va true
An enq can be done as long as vb is false; a deq can be done as long as va is true
Assume, if there is only one element in the FIFO it resides in da
db da
vb va

## Slide 25: Two-Element FIFO BSV code
module mkFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False);
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
method t first if va; return da;
endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
Can both enq and deq be ready at the same time?
yes
db da
vb va

## Slide 26: Two-Element FIFO Sequential behavior analysis
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
Suppose, initially vb=false and va=true (there is an element)
Suppose enq executes before deq
  enq executes: db <= x; vb <= True;
  deq executes: da <= x; vb <= False;
  Final values: da == x; db == x; va == True; vb == False;
Suppose deq executes before enq
  deq executes: va <= False;
  enq executes: da <= x; va <= True;
  Final values: da == x; db == ?; va == True; vb == False;
db da
vb va

## Slide 27: Two-Element FIFO concurrency analysis
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
no double-write error
Will concurrent execution of enq and deq cause a double write error?
  Initially vb=False and va=True
  enq will execute: db <= x; vb <= True;
  deq will execute va <= False;
  The final state will be va = False and vb = True; with the old data in da and new data in db
db da
vb va
oops!
we can’t get into this state if enq and deq are performed in some order

## Slide 28: Two-Element FIFO concurrency analysis - continued
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
  In this implementation, enq and deq should not be called concurrently
    later we will present a systematic procedure to decide which methods of a module can be called concurrently
  First, we will study when two rules that only use registers can be executed concurrently
db da
vb va

## Slide 29: Concurrent execution of rules
Two rules can execute concurrently, if concurrent execution would not cause a double-write error, and
The final state can be obtained by executing rules one-at-a-time in some sequential order

## Slide 30: Can these rules execute concurrently? (without violating the one-rule-at-a-time-semantics)
rule ra;
x <= x+1;
endrule
rule rb;
y <= y+2;
endrule
Final value of (x,y) (initial values (0,0))
Exam 1 Exam2 Exam3
Concurrent
Execution
ra<rb
rb<ra
Example 1
rule ra;
x <= y+1;
endrule
rule rb;
y <= x+2;
endrule
Example 2
rule ra;
x <= y+1;
endrule
rule rb;
y <= y+2;
endrule
Example 3
(1,2)
(1,2)
(1,2)
(1,2)
(1,3)
(3,2)
(1,2)
(1,2)
(3,2)
No Conflict
Conflict
ra<rb

## Slide 31: Rule scheduling
The BSV compiler schedules as many rules as possible for concurrent execution among the rules that are enabled (i.e., whose guards are true), provided it can ensure that the chosen rules don’t conflict with each other
Conflict:
  Double write
  If the effect of rule execution does not appear to be as if one rule executed after the other

## Slide 32: Scheduling, systematically
First register only, and with arbitrary modules

## Slide 33: some insight into Concurrent rule execution
There are more intermediate states in the rule semantics (a state after each rule step)
In the HW, states change only at clock edges
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 34: Parallel execution reorders reads and writes
In the rule semantics, each rule sees (reads) the effects (writes) of previous rules
In the HW, rules only see the effects from previous clocks, and only affect subsequent clocks
Rules
HW
clocks
rule
steps
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes

## Slide 35: Correctness
The compiler will schedule rules concurrently only if the net state change is equivalent to a sequential rule execution
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 36: Compiler test for concurrent rule execution James Hoe, Ph.D., 2000
Let RS(r) be the set of registers rule r may read
Let WS(r) be the set of registers rule r may write
Rules ra and rb are conflict free (CF) if
  (RS(ra)WS(rb) = )  (RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
Rules ra and rb are sequentially composable (SC) (ra<rb) if
(RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
If Rules ra and rb conflict if they are not CF or SC

## Slide 37: Compiler analysis
rule ra;
x <= x+1;
endrule
rule rb;
y <= y+2;
endrule
Exam 1 Exam2 Exam3
RS(ra) {x} {y} {y}
WS(ra) {x} {x} {x}
RS(rb) {y} {x} {y}
WS(rb) {y} {y} {y}
  RS(ra)WS(rb)  {y} {y}
  RS(rb)WS(ra)  {x} 
  WS(ra)WS(rb)   
  Conflict? CF C SC
Example 1
rule ra;
x <= y+1;
endrule
rule rb;
y <= x+2;
endrule
Example 2
rule ra;
x <= y+1;
endrule
rule rb;
y <= y+2;
endrule
Example 3

## Slide 38: Concurrent scheduling
The BSV compiler determines which rules among the rules whose guards are ready can be executed concurrently
It builds a simple greedy list-based scheduler:
  Picks the first enabled rule in the list
  Schedules the next enabled rule if it does not conflict with any of the rules scheduled so far
  Repeats the process until no more rules can be scheduled
Such a scheduler can be built as a pure combinational circuit, but it is not fair
In practice it does fine, and one can get around it programmatically
The list is built using textual ordering of rules but can be changed by user annotations

## Slide 39: Scheduling and Control Logic

## Slide 40: Compiling a Rule
f
x
current
state
next
state
d
p
guard
f
x
rule r (f.first() > 0) ;
x <= x + 1 ; f.deq ();
endrule
rdy signals,
read methods
next state values
Notes: In a circuit, pi maps to combination logic that looks at the current state and generates a boolean enable signal for this rule
The delta functions is another combination logic that computes the next state value from the current state value. Actually, delta has to compute the control signals to set the state element to the new value

## Slide 41: Combining State Updates: strawman
next state
value
flip-flop
enable
R
OR
p1
pn
d1,R
dn,R
OR
p’s from the rules
that update R
d’s from the rules
that update R
What if more than one rule is enabled?
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 42: Combining State Updates
next state
value
R
Scheduler:
Priority
Encoder
OR
f1
fn
p1
pn
d1,R
dn,R
OR
d’s from the rules
that update R
Scheduler ensures that at most one fi is true
p’s from all
the rules
one-rule-at-a-time
scheduler is
conservative
Enable for register R
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 43: Scheduling and control logic
Modules
(Current state)
Rules
d1
p1
Scheduler
f1
fn
p1
pn
Muxing
d1
dn
dn
pn
Modules
(Next state)
cond
action
“CAN_FIRE”
“WILL_FIRE”
Compiler synthesizes a scheduler such that at any given time f’s for only non-conflicting rules are true
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 44: Takeaway
One-rule-at-a-time semantics are very important to understand what behaviors a system can show
Efficient hardware for multi-rule system requires that many rules execute in parallel without violating the one-rule-at-time semantics
BSV compiler builds a scheduler circuit to execute as many rules as possible concurrently