## Slide 1
Constructive Computer Architecture:
Non-Pipelined Processors
Arvind & 6.1920 Staff
Electrical Engineering and Computer Science
Massachusetts Institute of Technology

## Slide 2: Single-Cycle RISC Processor
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
Datapath (arrows in this diagram) are conceptual; the real datapaths are derived automatically from the Bluespec description
2 read & 1 write ports
separate Instruction & Data memories
As an illustrative example, we use a subset of RISC-V 32-bit ISA.
Harvard Architecture
Notes: 2

## Slide 3: RISC-V Register States
32 general purpose registers (GPR)
  x0, x1, …, x31
  32-bit wide integer registers
  x0 is hard-wired to zero
Program counter (PC)
  32-bit wide
CSR (Control and Status Registers)
  mcycle
  minstret
  mhartid
  mtohost
  ...
We will not deal with CSRs in this subject

## Slide 4: Single-Cycle Implementation
module mkProcessor(Empty);
Reg#(Word) pc <- mkReg(0);
RFile2R1W rf <- mkRFile2R1W;
MagicMemory iMem <- mkMagicMemory;
MagicMemory dMem <- mkMagicMemory;
rule doProcessor;
let inst <- iMem.req(MemReq{op:Ld, addr:pc, data:dwv});
let dInst = decode(inst);
// dInst fields: iType, aluFunc, brFunc, dst, src1, src2, imm
let rVal1 = rf.rd1(dInst.src1);
let rVal2 = rf.rd2(dInst.src2);
let eInst = execute(dInst, rVal1, rVal2, pc);
// eInst fields: iType, dst, data, addr, nextPC
updateState(eInst, pc, rf, dMem);
endrule endmodule
computes values needed to update the processor state
instantiate the state
read the register file
actions to update the processor state
extracts the fields

## Slide 5: Every BSV program serves two purposes
It is a description from which a compiler can synthesize a hardware circuit
Like any program, it is a description which can be executed to produce an answer
  For example, the Single-cycle implementation can be simulated in software to execute any RISC-V program

## Slide 6: Understanding generated hardware (the real datapath)
Not all instructions have both src1 and src2 fields but there is no harm/cost in reading unused registers; we never use results of undefined fields
When the same function is called with two different arguments, a mux is generated automatically
rVal1
rVal2
RF
src1
src2
ALU
dInst
let rVal1 = rf.rd1(dInst.src1);
let rVal2 = rf.rd2(dInst.src2);
imm
Notes: 6
ALU should be split…

## Slide 7: Understanding generated hardware - continued
How many alu circuits?
  The two uses of alu are mutually exclusive, so the BSV compiler/backend tools should share the same alu circuit;
  Can address calculation use the same alu?
Reuse is not necessarily a good idea because it prevents specialization
  The circuit for pc+4 has a lot fewer gates than the circuit for pc+imm
case (iType)
OP: data = alu(rVal1, rVal2, aluFunc);
OPIMM: data = alu(rVal1, imm, aluFunc);
...
LOAD: begin addr = rVal1+imm; nextPc = pc+4; end
STORE: begin addr = rVal1+imm; data = rVal2;
nextPc = pc+4; end ...
Generally, we don’t concern ourselves with the sharing of combinational circuits
We could use the alu for this addition

## Slide 8: Instruction Decoding
An instruction can be executed only after each of its fields has been extracted
  Fields are needed to access the register file, compute address to access memory, supply the proper opcode to ALU, set the pc, ...
Some 32-bit values may not represent an instruction or may represent an instruction not supported by our implementation
Many instructions differ only slightly from each other in both decoding and execution
Unlike RISC-V, some instruction sets are extremely complicated to decode, e.g., Intel X86

## Slide 9: Decoding instructions An Example
What RISC-V instruction is represented by these 32 bits?
Reference manual specifies the fields as follows:
  opcode = 0110011
  funct3 = 000
  rd = 00011
  rs1 = 00010
  rs2 = 00001
What is the meaning of executing this instruction?
  => opCode Op, R-type encoding
  => ADD
  => x3
  => x2
opcode
00000000000100010000000110110011
rs1
rs2
funct3
funct7
rd
  => x1
rf.wr(3, alu(rf.rd1(2), rf.rd2(1), Add)); pc<=pc+4;

## Slide 10: Decoding Instructions: extract fields needed for execution
decode
instruction
brComp
rDst
rSrc1
rSrc2
imm
ext
aluFunc
iType
6:0
6:0,14:12,30
6:0, 14:12
11:7
19:15
24:20
31:7
Type DecodedInst
Bit#(32)
IType
AluFunc
Maybe#(RIndx)
Maybe#(RIndx)
Maybe#(RIndx)
BrFunc
Maybe#(Bit#(32))
pure combinational logic: derived automatically from the high-level description
Maybe type allows marking as valid or invalid
Notes: 10
Green is type…

## Slide 11: Decoded Instruction Type
typedef struct {
IType iType;
AluFunc aluFunc;
BrFunc brFunc;
Maybe#(RIndx) dst;
Maybe#(RIndx) src1;
Maybe#(RIndx) src2;
Maybe#(Data) imm;
} DecodedInst deriving(Bits, Eq);
typedef enum {Unsupported, Alu, Ld, St, J, Jr, Br, Auipc} IType deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Slt, Sltu, Sll, Sra, Srl} AluFunc deriving(Bits, Eq);
typedef enum {Eq, Neq, Lt, Ltu, Ge, Geu, AT, NT} BrFunc deriving(Bits, Eq);
Instruction groups with similar executions paths
Destination register 0 behaves like an Invalid destination
Notes: Here is the complete typedef:
typedef enum {Unsupported, Alu, Ld, St, J, Jr, Br, Csrr, Csrw, Auipc} IType deriving(Bits, Eq, FShow);
typedef enum {Eq, Neq, Lt, Ltu, Ge, Geu, AT, NT} BrFunc deriving(Bits, Eq, FShow);
typedef enum {Add, Sub, And, Or, Xor, Slt, Sltu, Sll, Sra, Srl} AluFunc deriving(Bits, Eq, FShow);
typedef struct {
IType iType;
AluFunc aluFunc;
BrFunc brFunc;
Maybe#(RIndx) dst;
Maybe#(RIndx) src1;
Maybe#(RIndx) src2;
Maybe#(CsrIndx) csr;
Maybe#(Data) imm;
} DecodedInst deriving(Bits, Eq, FShow);

## Slide 12: Internal names for various opcode and funct3 patterns
// opcode
Bit#(7) opOpImm = 7'b0010011; // OP-IMM
Bit#(7) opOp = 7'b0110011; // OP
Bit#(7) opLui = 7'b0110111; // LUI
Bit#(7) opAuipc = 7'b0010111; // AUIPC
Bit#(7) opJal = 7'b1101111; // JAL
Bit#(7) opJalr = 7'b1100111; // JALR
Bit#(7) opBranch = 7'b1100011; // BRANCH
Bit#(7) opLoad = 7'b0000011; // LOAD
Bit#(7) opStore = 7'b0100011; // STORE
// funct3
Bit#(3) fnADD = 3'b000; // ADD
Bit#(3) fnSLL = 3'b001; // SLL
Bit#(3) fnSLT = 3'b010; // SLT ……
Names and associated values are specified in the RISC-V ISA
...
names given by us
Notes: Better as enum…

## Slide 13: Decode Function
function DecodedInst decode(Bit#(32) inst);
let opcode = inst[ 6 : 0 ];
let rd = inst[ 11 : 7 ];
let funct3 = inst[ 14 : 12 ];
let rs1 = inst[ 19 : 15 ];
let rs2 = inst[ 24 : 20 ];
let aluSel = inst[ 30 ]; // Add/Sub, Srl/Sra
Bit#(32)immI=…; Bit#(32)immS=…; Bit#(32)immB=…;
Bit#(32)immU=…; Bit#(32)immJ=…; // I/S/B/U/J-imm
DecodedInst dInst = ?;
case (opcode)
opOp
...
endcase
return dInst;
endfunction
initially undefined
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7

## Slide 14: Decoding Instructions
case (opcode)
opOpImm: …
opOp: …
opLui: …
opAuipc: …
opJal: …
opJalr: …
opBranch: …
opLoad: …
opStore: …
default: … // Unsupported
endcase
// opcode
Bit#(7) opOpImm = 7'b0010011;
Bit#(7) opOp = 7'b0110011;
Bit#(7) opLui = 7'b0110111;
Bit#(7) opAuipc = 7'b0010111;
Bit#(7) opJal = 7'b1101111;
Bit#(7) opJalr = 7'b1100111;
Bit#(7) opBranch = 7'b1100011;
Bit#(7) opLoad = 7'b0000011;
Bit#(7) opStore = 7'b0100011;

## Slide 15: Decoding Instructions: Computational Instructions
opOp: begin
dInst.iType = Alu;
dInst.aluFunc = case (funct3)
fnAND: And;
fnSLTU: Sltu;
…
fnADD: aluSel == 0 ? Add : Sub;
fnSR: aluSel == 0 ? Srl : Sra;
endcase;
dInst.brFunc = NT;
dInst.dst = Valid rd;
dInst.src1 = Valid rs1;
dInst.src2 = Valid rs2;
dInst.imm = Invalid;
end
Decoding instructions with immediate operand (i.e., opcode = OP-IMM) is similar
Valid ImmI;
Invalid;
Add;
opOpImm:

## Slide 16: Decoding Instructions: Unconditional Jumps
opJal: begin
dInst.iType = J;
dInst.aluFunc = ?;
dInst.brFunc = AT;
dInst.dst = Valid rd;
dInst.src1 = Invalid;
dInst.src2 = Invalid;
dInst.imm = Valid immJ;
end
opJalr: begin
dInst.iType =
dInst.aluFunc =
dInst.brFunc =
dInst.dst =
dInst.src1 =
dInst.src2 =
dInst.imm =
end
Jr;
?;
AT;
Valid rd;
Valid rs1;
Invalid;
Valid immI;
Jump indirect through register
Jump to pc+offset

## Slide 17: Decoding Instructions: Conditional Branch
opBranch: begin
Maybe#(BrFunc) brF =
case(funct3)
fnBEQ: Valid Eq;
…
fnBGEU: Valid Geu;
default: Invalid;
endcase;
dInst.iType =
dInst.aluFunc =
dInst.brFunc =
dInst.dst = Invalid;
dInst.src1 = Valid rs1;
dInst.src2 = Valid rs2;
dInst.imm = Valid immB;
end
isValid(brF) ? Br : Unsupported;
?;
fromMaybe(?, brF);

## Slide 18: Decoding Instructions: Load & Store
opLoad: begin // only support LW
dInst.iType = funct3 == fnLW ? Ld : Unsupported;
dInst.aluFunc = Add; // calc effective addr
dInst.brFunc = NT;
dInst.dst = Valid rd;
dInst.src1 = Valid rs1;
dInst.src2 = Invalid;
dInst.imm = Valid immI;
end
opStore: begin // only support SW
dInst.iType = funct3 == fnSW ? St : Unsupported;
dInst.aluFunc = Add; // calc effective addr
dInst.brFunc = NT;
dInst.dst =
dInst.src1 =
dInst.src2 =
dInst.imm =
end
Invalid;
Valid rs1;
Valid rs2;
Valid immS;

## Slide 19: Decoding instructions: Unsupported
default: begin
dInst.iType = Unsupported;
dInst.aluFunc = ?;
dInst.brFunc = NT;
dInst.dst = Invalid;
dInst.src1 = Invalid;
dInst.src2 = Invalid;
dInst.imm = Invalid;
end
Notes: 19

## Slide 20: Reading Registers and Executing Instructions
execute
dInst
addr
brTaken
data
iType
dst
ALU
Branch
Address
pc
rVal2
rVal1
Pure combinational logic
either for memory reference or branch target
either for rf write or St
ALUBr
RF
src2
src1
Notes: 20
ALU should be split…

## Slide 21: Output type of exec function
typedef struct {
IType iType;
Maybe#(RIndx) dst;
Data data;
Addr addr;
Bool brTaken;
} ExecInst deriving(Bits, Eq);
Notes: Here is the complete typedef:
typedef struct {
IType iType;
Maybe#(RIndx) dst;
Maybe#(CsrIndx) csr;
Data data;
Addr addr;
Bool mispredict;
Bool brTaken;
} ExecInst deriving(Bits, Eq, FShow);

## Slide 22: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1, Data rVal2,
Addr pc);
ExecInst eInst = ?;
Data aluVal2 =
let aluRes =
eInst.iType =
eInst.data =
eInst.brTaken =
let brAddr =
eInst.addr =
eInst.dst =
return eInst;
endfunction
fromMaybe(rVal2, dInst.imm);
alu(rVal1, aluVal2, dInst.aluFunc);
dInst.iType;
dInst.iType==St? rVal2 :
(dInst.iType==J||dInst.iType==Jr)? (pc+4):
dInst.iType==Auipc ?
(pc+fromMaybe(?, dInst.imm)) : aluRes;
aluBr(rVal1, rVal2, dInst.brFunc);
brAddrCalc(pc, rVal1, dInst.iType,
fromMaybe(?, dInst.imm));
(dInst.iType==Ld || dInst.iType==St)?
aluRes : brAddr;
dInst.dst;
Notes: Add Auipc in eInst.data

## Slide 23: Branch Address Calculation
function Addr brAddrCalc(Addr pc, Data val,
IType iType, Data imm);
Addr targetAddr = case (iType)
J : {pc + imm};
Jr : {truncateLSB(val + imm), 1'b0};
Br : pc + imm;
default: error; //32’hAAAAAAAA
endcase;
return targetAddr;
endfunction
Half word aligned;
Maybe needed to support compressed instruction format
Notes: 23
Change last case to default
Br: pc+imm (not pc+4+imm)

## Slide 24: Single-Cycle RISC-V atomic state updates
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld,
addr: eInst.addr, data: ?});
else if (eInst.iType == St) let dummy <- dMem.req(MemReq{op: St,
addr: eInst.addr, data: data});
if(isValid(eInst.dst)) rf.wr(fromMaybe(?, eInst.dst), eInst.data); let nextPC = eInst.brTaken ? eInst.addr: pc + 4;
pc <= nextPC;
endrule
endmodule
state updates
The whole processor is described using one rule; lots of big combinational functions
Notes: 24

## Slide 25: Variations on non-pipelined microarchitectures

## Slide 26: Princeton Architecture instructions and data reside in the same memory
PC
Decode
Register File
Execute
Magic
Memory
We can’t do instruction fetch and LD/ST at the same time because there is only one memory
Such resource conflicts are known as structural hazards and require multicycle implementation
Extra registers are required to hold values between cycles
Memory instructions can’t be executed in one cycle!
Notes: 26

## Slide 27: Princeton Architecture introduce intermediate state
Every instruction takes two cycles: Fetch followed by Execute
Insert f2d register to hold the fetched instruction
A one bit register to record the state of the instruction
f2d
state
PC
Decode
Register File
Execute
Magic
Memory
typedef enum {Fetch, Execute} State deriving (Bits, Eq);
Notes: 27

## Slide 28: Princeton Architecture Two-cycle
module mkProcPrincetonTwoCycle(Empty);
Code to instantiate pc, rf, magic mem
Reg#(Word) f2d <- mkRegU;
Reg#(State) state <- mkReg(Fetch);
rule doFetch if (state == Fetch);
Code to fetch the instruction at pc
f2d <= inst;
state <= Execute;
endrule
rule doExecute if (state == Execute);
Code to decode the instruction in f2d, execute, updateState
state <= Fetch;
endrule
endmodule
If state is Fetch then fetch the instruction and put it in f2d, and change the state to Execute
If state is Execute then execute the instruction in f2d, and change the state to Fetch

## Slide 29: doExecute rule reexamined
rule doExecute if (state == Execute);
let inst = f2d;
let dInst = decode(inst);
let rVal1 = rf.rd1(dInst.src1);
let rVal2 = rf.rd2(dInst.src2);
let eInst = execute(dInst, rVal1, rVal2, pc);
//Extract fileds of eInst: data, addr, dst;
// memory access
if (eInst.iType == LOAD) begin
data <- dMem.req(MemReq{op:Ld, addr:addr, data: dwv});
end else if (eInst.iType == STORE) begin
let dummy <- dMem.req(MemReq{op:St, addr:addr, data:data});
end
// register file write
if (dst.valid) rf.wr(dst.index, data);
// pc update
pc <= eInst.nextPc; state <= Fetch;
endrule
Execution of all instructions except LD/ST can be completed in the Fetch cycle
PC
Decode
Register File
Execute
Magic
Memory
f2d
state
updateState(eInst,pc,rf,dMem) expanded

## Slide 30: Another Princeton Architecture: where non-memory instructions take one cycle
Do fetch, decode, and execute in one cycle for all non-memory instructions; no need for f2d
For a memory instruction:
  after fetch, decode and execute, put the partially executed instruction in a register (e2m)
  In the next cycle, do the memory operation, update the register file and pc
e2m
The datapath for e2m is not accurate
PC
Decode
Register File
Execute
Magic
Memory
f2d
state
Notes: 30

## Slide 31: Princeton Architecture where non-memory instructions take one cycle
rule doFetch if (state == FetchExecute);
let inst <- mem.req(MemReq{op: Ld, addr: pc, data: dwv});
let dInst = decode(inst);
let rVal1 = rf.rd1(dInst.src1); //similarly rVal2
let eInst = execute(dInst, rVal1, rVal2, pc);
if (eInst.iType==Ld) || (eInst.iType==St) begin
e2m <= eInst;
state <= MemoryAccess;
end else begin
if (eInst.dst.valid) rf.wr(eInst.dst.index, eInst.data);
pc <= eInst.nextPc;
state <= FetchExecute;
end
Endrule
rule doMemoryAccess if (state == MemoryAccess);
updateState(e2m, pc, rf, mem);
state <= FetchExecute;
endrule
Save the executed instruction state in e2m register
The code

## Slide 32: Performance implications
Suppose fraction f of N executed instructions are memory access instructions
  Two-cycle Princeton architecture will take 2N cycles
  How many cycles will the variable-cycle Princeton architecture take?
f*2*N + (1-f)*N
= (1+f)*N
As far as the performance is concerned, cycle counts in not the whole story; one needs to compare the cycle times of the two designs as well
More to come later

## Slide 33: Realistic Memory Interface Request/Response methods
interface Memory;
method Action req(MemReq req);
method ActionValue#(Word) resp();
endinterface
typedef struct {MemOp op; Word addr; Word data;}
MemReq deriving(Bits, Eq);
typedef enum {Ld, St} MemOp deriving(Bits, Eq);
No response for Stores;
Load responses come back in the requested order
op
address
data(store)
en
rdy
req
memory
resp
data (load)
en
rdy
m.req(MemReq{op:Ld, addr:a, data:dwv});
m.req(MemReq{op:St, addr:a, data:v});
let data <- m.resp();

## Slide 34: Princeton architecture with a realistic memory
With request/response memory even instruction fetch cannot be completed in one cycle
  Instruction fetch must be split into two rules – send request and receive response
  Need registers to hold the state of a partially executed instructions
PC
Decode
Register File
Execute
Memory
state
req
resp
Notes: 34

## Slide 35: Processor with realistic memory
module mkProcPrincetonMulticycle(Empty);
Code to instantiate pc, rf, mem, and registers that hold
the state of a partially executed instruction
rule doFetch if (state == Fetch);
Code to initiate instruction fetch; go to Execute
rule doExecute if (state == Execute);
let inst <- mem.resp;
Code to 1. execute all instructions except memory
instructions; go to Fetch
Or 2. initiate memory access;
go to Fetch (Store) OR go to LoadWait (Load)
rule doLoadWait if (state == LoadWait);
Code to wait for the load value, update rf, go to Fetch
endmodule

## Slide 36: Multicycle ALU’s multicycle or floating point ALU operations
Multicycle ALU’s can be viewed as request/response modules
Instructions can be further classified after decoding as simple 1 cycle, multicycle (e.g., multiply) or memory access
PC
Decode
Register File
Execute
Memory
state
req
resp
Notes: 36

## Slide 37: Processor with realistic memory and multicycle ALUs
module mkProcMulticycle(Empty);
Code to instantiate pc, rf, mem, and registers to hold the
state of a partially executed instruction
rule doFetch if (state == Fetch);
Code to initiate instruction fetch; go to Execute
rule doExecute if (state == Execute);
let inst <- mem.resp;
Code to 1. execute all instructions except
memory and multicycle instructions; go to Fetch
Or 2. initiate memory access
go to Fetch (Store) OR go to LoadWait (Load)
Or 3. initiate multicycle instruction; go to MCWait
rule doLoadWait if (state == LoadWait);
Code to wait for the load value, update rf, go to Fetch
rule doMCWait if (state == MCWait);
Code to wait for MC value, update rf, go to Fetch
endmodule

## Slide 38: Clock speed
Clock speed depends upon the longest combinational path between two state elements. Thus, in a single cycle implementation
Clock in a two-cycle implementation may be faster
tClock > tM + tDEC + tRF + tALU+ tM+ tWB
tClock > max {tM , (tDEC + tRF + tALU+ tM+ tWB )}
However, this may not improve the performance because now some instructions will take two cycles to execute
PC
Decode
Register File
Execute
Memory
state
req
resp
Notes: 38

## Slide 39: Cycle counts
Different instructions take different number of cycles in our designs
  Depending upon the type of opcode, an instruction has to go through 1 to 3 processor-rule firings
  The number of cycles between processor-rule firings depends on how quickly the memory responds or a multicycle functional unit completes its work for the input data
Next, we will study pipelining

## Slide 40: Processor Interface
For testing, processor is connected to a host computer* which can read and write the memory of the processor directly
The processor’s memory is preloaded with program and data; it always starts at pc=0
When the program terminates it writes a 0 in a predetermined location and stops the simulation
  If the program hits an illegal or unsupported instruction, it dumps the processor state and stops the simulation
Consequently, the processor interface has no methods, ie, its interface is Empty!
*In the simulation environment the host computer is the same computer on which the simulator runs
module mkProcessor(Empty);
...
endmodule

## Slide 41: Extras

## Slide 42: Instruction Formats
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
R-type instruction
I-type instruction & I-immediate (32 bits)
S-type instruction & S-immediate (32 bits)
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
S-imm = signExtend({inst[31:25], inst[11:7]})
I-imm = signExtend(inst[31:20])

## Slide 43: Instruction Formats cont.
SB-type instruction & B-immediate (32 bits)
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7
B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
U-type instruction & U-immediate (32 bits)
rd
opcode
5
7
imm[31:12]
20
U-imm = signExtend({inst[31:12], 12’b0})
UJ-type instruction & J-immediate (32 bits)
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
J-imm = signExtend({inst[31], inst[19:12], inst[20], inst[30:21], 1’b0})

## Slide 44: Computational Instructions cont.
Register-immediate instructions (U-type)
  opcode = LUI : rd  U-imm
  opcode = AUIPC : rd  pc + U-imm
  U-imm = {inst[31:12], 12’b0}
rd
opcode
5
7
imm[31:12]
20

## Slide 45: Computational Instructions
Register-Register instructions (R-type)
  opcode=OP: rd  rs1 (funct3, funct7) rs2
  funct3 = SLT/SLTU/AND/OR/XOR/SLL
  funct3= ADD
    funct7 = 0000000: rs1 + rs2
    funct7 = 0100000: rs1 – rs2
  funct3 = SRL
    funct7 = 0000000: logical shift right
    funct7 = 0100000: arithmetic shift right
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7

## Slide 46: Computational Instructions cont
Register-immediate instructions (I-type)
  opcode = OP-IMM: rd  rs1 (funct3) I-imm
  I-imm = signExtend(inst[31:20])
  funct3 = ADDI/SLTI/SLTIU/ANDI/ORI/XORI
A slight variant in coding for shift instructions - SLLI / SRLI / SRAI
  rd  rs1 (funct3, inst[30]) I-imm[4:0]
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Notes: What is the role of inst[30]?

## Slide 47: Control Instructions
  Unconditional jump and link (UJ-type)
  opcode = JAL: rd  pc + 4; pc  pc + J-imm
  J-imm = signExtend({inst[31], inst[19:12], inst[20], inst[30:21], 1’b0})
  Jump ±1MB range
Unconditional jump via register and link (I-type)
  opcode = JALR: rd  pc + 4; pc  (rs1 + I-imm) & ~0x01
  I-imm = signExtend(inst[31:20])
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Notes:   Effect of ~0x01

## Slide 48: Control Instructions cont.
Conditional branches (SB-type)
  opcode = BRANCH: pc  compare(funct3, rs1, rs2) ? pc + B-imm : pc + 4
  B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
  Jump 4KB range
  funct3 = BEQ/BNE/BLT/BLTU/BGE/BGEU
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7

## Slide 49: Load & Store Instructions
Load (I-type)
  opcode = LOAD: rd  mem[rs1 + I-imm]
  I-imm = signExtend(inst[31:20])
  funct3 = LW/LB/LBU/LH/LHU
Store (S-type)
  opcode = STORE: mem[rs1 + S-imm]  rs2
  S-imm = signExtend({inst[31:25], inst[11:7]})
  funct3 = SW/SB/SH
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
Notes: Ignore byte and half word instructions: LB, LBU, LH, LHU, SB, SH

## Slide 50: Magic Memory Model
Reads and Writes behave as in a register file (not true for real SRAM or DRAM)
  Reads are combinational
  Write, if enabled, is performed at the rising clock edge
However, unlike a register file, there is only one port, which is used either for reading or for writing
MAGIC
RAM
ReadData
WriteData
Address
WriteEnable
Clock

## Slide 51: Magic Memory Interface
interface MagicMemory;
method ActionValue#(Word) req(MemReq r);
endinterface
typedef struct {MemOp op; Word addr; Word data;}
MemReq deriving(Bits, Eq);
typedef enum {Ld, St} MemOp deriving(Bits, Eq);
Magic memory can be read or written any time, so the guards are always true (not shown)
memReq
magic memory
load data
op
address
store data
en
let data <- m.req(MemReq{op:Ld, addr:a, data:?});
let dummy <- m.req(MemReq{op:St, addr:a, data:v});