## Slide 1
Constructive Computer Architecture
Caches and store buffers
Arvind and Thomas (EPFL)
Electrical Engineering and Computer Science
Massachusetts Institute of Technology

## Slide 2: Memory Hierarchy
size: RegFile << SRAM << DRAM
latency: RegFile << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  hit (data Î fast memory)  low latency access
  miss (data Ï fast memory)  long latency access (DRAM)
Small,
Fast Memory
SRAM
CPU
RegFile
Big, Slow Memory
DRAM
holds frequently used data
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 3: Managing fast storage
User managed Scratchpad memory
  ISA is aware of the storage hierarchy; separate instructions are needed to access different storage levels
Automatically managed Cache memory:
  programmer has little control over how data moves between fast and slow memory
  Historically very successful (painless for the programmer)

## Slide 4: A typical memory organization
I-cache often returns more words than one
We will first study a simple data cache
I-cache
CPU, RegFile
DRAM
D-cache
32 bits words
512 bits
line
line

## Slide 5: Inside a Cache
cache line
tag data
Data from locations 100, 101, ...
Data
Byte
Data
Byte
Data
Byte
100
304
6848
A cache line usually holds more than one word
  Tag bits identify a cache line
  Spatial locality: if address x is referenced then addresses x+1, x+2 etc. are very likely to be referenced in the near future
    consider instruction streams, array and record accesses
  Larger data sets can be transported more efficiently
Notes: Tag only needs enough bits to uniquely identify the block (jse)

## Slide 6: Extracting cache tags & index
Processor requests are for a single word, but cache line size is 2L words (typically L is 2 to 4 words)
Processor uses word-aligned byte addresses, i.e., the two least significant bits of the address are 00
Need getIndex, getTag, getOffset functions
tag index L 2
Cache size in bytes
Byte addresses

## Slide 7: Direct-Mapped Cache The simplest implementation
Tag
Data Block
V
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Cache line number
What is a bad reference pattern?
Strided and
stride = size of cache
req address
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)

## Slide 8: Loads
Search the cache for the processor generated address
Found in cache
a.k.a. hit
Return a copy of the word from the cache-line
Not in cache
a.k.a. miss
Bring the missing cache-line from Main Memory
  May first require writing back a cache-line to create space
…
Update cache and
return word to processor

## Slide 9: Stores
On a write hit:
  write only to cache and update the next level memory when the line is evacuated
On a write miss:
  allocate – because of multi-word lines we first fetch the line, and then update a word in it
Notes: Write through vs. write back
WT:
+read miss never results in writes to main memory + main memory always has the most current copy of the data (consistent) - write is slower - every write needs a main memory access - as a result uses more memory bandwidth
WB:
+ writes occur at the speed of the cache memory + multiple writes within a block require only one write to main memory + as a result uses less memory bandwidth - main memory is not always consistent with cache - reads that result in replacement may cause writes of dirty blocks to main memory
Write Back with No Write Allocate: on hits it writes to cache setting dirty bit for the block, main memory is not updated; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the same block, if the block originally caused a miss, will generate misses all the way and result in very inefficient execution.
Hence, WB+WA more common combination.
Write Through with No Write Allocate: on hits it writes to cache and main memory; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the block will update main memory anyway, so write misses aren’t helped. Only read misses helped with allocate.
Hence, WT, no WA usually.
Re-look at these options when the next level is a cache; not a memory.
Write back with no allocate? Why is this

## Slide 10: Blocking vs. Non-Blocking cache
Blocking cache:
  At most one outstanding miss
  Cache must wait for memory to respond
  Cache does not accept requests in the meantime
Non-blocking cache:
  Multiple outstanding misses
  Cache can continue to process requests while waiting for memory to respond to misses
We will outline a write-back, Write-miss allocate, Direct-mapped, blocking cache

## Slide 11: Cache Interface
interface Cache; method Action req(MemReq r);
// (op: Ld/St, addr: ..., data: ...)
method ActionValue#(Data) resp;
// no response for St
method ActionValue#(MemReqL) memReq;
method Action memResp(Line r);
endinterface
cache
req
resp
memReq
memResp
Processor
DRAM or next level cache
hitQ
mReqQ
mRespQ
mshr
Miss request Handling Register(s)
Requests are tagged for non-blocking caches
Can be replaced by first and deq methods
Notes: Miss Status Handling Registers (MSHRs)

## Slide 12: Interface dynamics
The cache either gets a hit and responds immediately, or it gets a miss, in which case it takes several steps to process the miss
Reading the response dequeues it
  Resp can be replaced by first and deq methods
Methods are guarded, e.g., cache may not be ready to accept a request because it is processing a miss
A mshr register keeps track of the state of the request while it is being processed
typedef enum {Ready, StartMiss, SendFillReq, WaitFillResp} ReqStatus deriving (Bits, Eq);

## Slide 13: Blocking cache state elements
Build dataArray to hold the data;
Build tagArray to hold the tags;
Build dirtyArray to record which lines have been written;
FIFO#(Data) hitQ <- mkBypassFIFO;
Reg#(MemReq) missReq <- mkRegU;
Reg#(ReqStatus) mshr <- mkReg(Ready);
FIFO#(MemReq) memReqQ <- mkFIFO;
FIFO#(Line) memRespQ <- mkFIFO;
CF Fifos are preferable because they provide better decoupling. An extra cycle here may not affect the performance by much
Tag and valid bits could be kept together as a Maybe type
mshr and missReq go together

## Slide 14: Req method Blocking cache
method Action req(MemReq r) if(mshr == Ready);
extract idx, tag, wOffset, currTag from r
if (hit) then
read dataArray at idx
if(r.op == Ld) enque x[wOffset]) in hitQ
else // St operation
overwrite the appropriate word in line;
update dataArray and dirtyArray
else begin missReq <= r; mshr <= StartMiss; end
endmethod

## Slide 15: Miss processing
mshr = StartMiss 
  if the slot is occupied by dirty data, initiate a write back of data
  mshr <= SendFillReq
mshr = SendFillReq 
  send request to the memory
  mshr <= WaitFillReq
mshr = WaitFillReq 
  Fill the slot when the data is returned from the memory and put the load response in hitQ
  mshr <= Ready
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready

## Slide 16: Start-miss and Send-fill rules
rule startMiss(mshr == StartMiss);
extract idx from missing address;
extract tag from tagArray;
extract dirty bit from dirtyArrar;
if tag is valid and line is dirty // write-back
enque a store request for the dirty line in memReqQ;
mshr <= SendFillReq;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule sendFillReq (mshr == SendFillReq);
memReqQ.enq(missReq); mshr <= WaitFillResp;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready

## Slide 17: Wait-fill rule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule waitFillResp(mshr == WaitFillResp);
extract idx and tag from missReq.addr;
let data = memRespQ.first;
update tagArray at idx;
if miss request is Ld then
update dirtyArray and dataArray;
enque appropriate word from data in hitQ;
else // miss request is St
update the word in line;
update dirtyArray and dataArray;
memRespQ.deq;
mshr <= Ready;
endrule
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 18: Rest of the methods
method ActionValue#(Data) resp;
hitQ.deq;
return hitQ.first;
endmethod
method ActionValue#(MemReq) memReq;
memReqQ.deq;
return memReqQ.first;
endmethod
method Action memResp(Line r);
memRespQ.enq(r);
endmethod
Memory side methods

## Slide 19: Hit and miss performance
Hit
  Directly related to the latency of L1
  0-cycle latency if hitQ is a bypass FIFO
Miss
  No evacuation: memory load latency plus combinational read/write
  Evacuation: memory store followed by memory load latency plus combinational read/write
Adding a few extra cycles in the miss case does not have a big impact on performance

## Slide 20: Plan for the rest of the lecture
Store Buffers
Different write policies
Associative caches
Quick overview of non-blocking caches
Another abstraction for cache implementation

## Slide 21: Speeding up Store Misses
Unlike a load, a store does not require memory system to return any data to the processor; it only requires the cache to be updated for future load accesses
Instead of delaying the pipeline, a store can be performed in the background; In case of a miss the data does not have to be brought into L1 at all (Write-miss no allocate policy)
mReqQ
mRespQ
L1
Store buffer(stb)
a small FIFO of (a,v) pairs
Core

## Slide 22: Store Buffer
A St req is enqueued into stb
  input reqs are blocked if there is no space in stb
A Ld req searches stb, and then L1;
  If Ld gets a hit in stb – it selects the most recent matching entry
  If Ld gets a miss in stb search in L1, the L1 result is returned
  If no match in either stb and L1, miss-processing commences
In background, oldest store in stb is dequed and processed
  If St address hits in L1: update L1; if write-through, then also send to it to memory
  If it misses:
    Write-back write-miss-allocate: fetch the cache line from memory (miss processing) and then process the store
    Write-back/Write-through write-miss-no-allocate: pass the store to memory
mReqQ
mRespQ
L1
Store buffer(stb)
a small FIFO of (a,v) pairs

## Slide 23: L1+Store Buffer (write-back, write-miss-allocate): Req method
method Action req(MemReq r) if(mshr == Ready);
... get idx, tag and wOffset
if (request is a Ld) // search stb
x = stb.search(r.addr);
if (x is valid) then enque x in hitQ;
else // search L1
if (hit) then
enqueue the appropriate word in hitQ;
else missReq <= r; mshr <= StartMiss;
else // the request is a St
enqueue <addr, data> in stb
endmethod

## Slide 24: L1+Store Buffer (write-back, write-miss-allocate): Exit from Store Buff
rule mvStbToL1 (mshr == Ready);
let the first element in stb be <addr,data>;
stb.deq;
// move the oldest entry of stb into L1
// may start allocation/evacuation
... get idx, tag and wOffset
if (hit) then
update dataArray and dirtyArray
else missReq <= r;
mshr <= StartMiss;
endrule

## Slide 25: Give priority to req method in accessing L1
method Action req(MemReq r) if(mshr == Ready);
... get idx, tag and wOffset
if(request is Ld) // search stb
let x = stb.search(r.addr);
if (isValid(x)) then enqueue x in hitQ;
else // search L1
...
else // the request is a St
enqueue <addr, data> in stb
endmethod
lockL1[0] <= True;
rule clearL1Lock; lockL1[1] <= False; endrule
&& !lockL1[1]
Lock L1 while processing processor requests
rule mvStbToL1 (mshr == Ready);
let the first element in stb be <addr,data>;
stb.deq; ... get idx, tag and wOffset and store in L1
endrule

## Slide 26: Write Policy
Write-through: CPU writes are cached, but also written to main memory immediately; Memory always holds current contents
Write-back: CPU writes are cached, but not written to main memory until we replace the line. Memory contents can be “stale”
  Upon replacement, a modified cache line must first be written back to memory before loading the new cache line
  To avoid unnecessary writebacks, a Dirty bit is added to each cache line to indicate if the value has been modified since it was loaded from memory
No cache write on a Write-miss: On a cache miss, write is sent directly to the memory without a cache write
Write-back is the most commonly used policy, because it saves cache<->memory bandwidth
Notes: dsm: Slide used to say 90% of cache ops are reads. Nope. On systems with wback caches, ~10% of the LLC or mem traffic is typically writes. But that doesn’t mean stores are rare!
------
Okay, one more cache design decision to make, then we’re done!
How should we handle memory writes in the cache? Ultimately we’ll
need update main memory with the new data, but when should that
happen?
The most obvious choice is to perform the write immediately. In other
words, whenever the CPU sends a write request to the cache, the cache
then performs the same write to main memory. This is called
“write-through”. That way main memory always has the most up-to-date
value for all locations. But this can be slow if the CPU has to wait
for a DRAM write access — writes could become a real bottleneck! And
what if the program is constantly writing a particular memory
location, e.g., updating the value of a local variable in the current
stack frame? In the end we only need to write the last value to main
memory. Writing all the earlier values is waste of memory bandwidth.
[CLICK] Suppose we let the CPU continue execution while the cache
waits for the write to main memory to complete — this is called
“write-behind”. This will overlap execution of the program with the
slow writes to main memory. Of course, if there’s another cache miss
while the write is still pending, everything will have to wait at that
point until both the write and subsequent refill read finish, since
the CPU can’t proceed until the cache miss is resolved.
[CLICK] The best strategy is called “write-back” where the contents of
the cache are updated and the CPU continues execution immediately.
The updated cache value is only written to main memory when the cache
line is chosen as the replacement line for a cache miss. This
strategy minimizes the number of accesses to main memory, preserving
the memory bandwidth for other operations. This is the strategy used
by most modern processors.

## Slide 27: Associative caches

## Slide 28: Direct-Mapped Cache Problem: Conflict Misses
Loop A:
Code at 1024, data at 37
Assume:
1024-line DM cache
line size = 1 word
Consider looping code, in steady state
Assume WORD, not BYTE, addressing
Word
Address
1024
37
1025
38
1026
39
1024
37
…
Cache
Line index
0
37
1
38
2
39
0
37
Hit/
Miss
HIT
HIT
HIT
HIT
HIT
HIT
HIT
HIT
Inflexible mapping (each address can only be in one cache location)  Conflict misses!
Loop B:
Code at 1024, data at 2048
1024
2048
1025
2049
1026
2050
1024
2048
...
0
0
1
1
2
2
0
0
MISS
MISS
MISS
MISS
MISS
MISS
MISS
MISS
Notes: DM caches do have an Achilles heel. Consider running the
3-instruction LOOPA code with the instructions located starting at
word address 1024 and the data starting at word address 37 where the
program is making alternating accesses to instruction and data, e.g.,
a loop of LD instructions.
Assuming a 1024-line DM cache with a line size of 1, the steady state
hit ratio will be 100% once all six locations have been loaded into
the cache since each location is mapped to a different cache line.
[CLICK] Now consider the execution of the same program, but this time
the data has been relocated to start at word address 2048. Now the
instructions and data are competing for use of the same cache lines.
[CLICK] For example, the first instruction (at address 1024) and the
first data word (at address 2048) both map to cache line 0, so only
one them can be in the cache at a time. So fetching the first
instruction fills cache line 0 with the contents of location 1024, but
then the first data access misses and then refills cache line 0 with
the contents of location 2048. The data address is said to “conflict”
with the instruction address. The next time through the loop, the
first instruction will no longer be in the cache and it’s fetch will
cause a cache miss, called a “conflict miss”. So in the steady state,
the cache will never contain the word requested by the CPU.
This is very unfortunate! We were hoping to design a memory system
that offered the simple abstraction of a flat, uniform address space.
But in this example we see that simply changing a few addresses
results in the cache hit ratio dropping from 100% to 0%. The
programmer will certainly notice her program running 10 times slower!
So while we like the simplicity of DM caches, we’ll need to make some
architectural changes to avoid the performance problems caused by
conflict misses.

## Slide 29: N-way Set-Associative Cache
Use multiple direct-mapped caches in parallel to reduce conflict misses
Nomenclature:
  # Rows = # Sets
  # Columns = # Ways
  Set size = #ways = “set associativity” (4-way  4 lines/set)
Each address maps to only one set, but can
be in any way within the set
Tags from all ways are checked in parallel
Fully-associative cache: Number of ways = Number of lines
  Any address can be in any line  No conflict misses, but expensive
8 sets
4 ways
Tag
Line
Tag
Line
Tag
Line
Tag
Line
=?
=?
=?
=?
INCOMING ADDRESS
tag
index
Notes: The result would be what we call an 4-way set-associative (SA) cache.
An N-way SA cache is really just N DM caches (let’s call them
sub-caches) operating in parallel. Each of the N sub-caches compares
the tag field of the incoming address with the tag field of the cache
line selected by the index bits of the incoming address. The N cache
lines searched on a particular request form a search “set” and the
desired location might be held in any member of the set.
The 4-way SA cache shown here has 8 cache lines in each sub-cache, so
each set contains 4 cache lines (one from each sub-cache) and there
are a total of 8 sets (one for each line of the sub-caches).
An N-way SA cache can accommodate up to N lines whose addresses map
to the same cache index. So access to up to N lines with conflicting
addresses can still be accommodated in this cache without misses.
This a big improvement over a DM cache where an address conflict will
cause the current resident of a cache line to be evicted in favor of
the new request.
And an N-way SA cache can have a very large number of cache lines but
still only have to pay the cost of N tag comparators. This is a big
improvement over a FA cache where a large number of cache lines would
require a large number of comparators.
So N-way SA caches are a good compromise between a conflict-prone DM
cache and the flexible but very expensive FA cache.

## Slide 30: Associativity Implies Choices
Compare addr with only one tag
Location A can be stored in exactly one cache line
Issue: Replacement Policy
address
Fully associative
address
Direct-mapped
N
address
N-way set-associative
Compare addr with N tags simultaneously
Location A can be stored in exactly one set, but in any of the N cache lines belonging to that set
Compare addr with each tag simultaneously
Location A can be stored in any cache line
Notes: There’s one final issue to resolve with SA and FA caches. When
there’s a cache miss, which cache line should be chosen to hold the
data that will be fetched from main memory? That’s not an issue with
DM caches, since each data line can only be held in one particular
cache line, determined by its address. But in N-way SA caches, there
are N possible cache lines to choose from, one in each of the ways.
And in a FA cache, any of the cache lines can be chosen.
So, how to choose? Our goal is to choose to replace the contents of
the cache line which will minimize the impact on the hit ratio in the
future.

## Slide 31: Replacement Policies
Least Recently Used (LRU): Replace the line that was accessed furthest in the past
  Works well in practice
  Need to keep ordered list of N items → N! orderings → O(log2N!) = O(N log2N) “LRU bits” + complex logic
  Caches often implement cheaper approximations of LRU
Other policies:
  First-In, First-Out (least recently replaced)
  Random: Choose a candidate at random
    Not very good, but does not have adversarial access patterns
Notes: The optimal choice is to replace the line that is accessed furthest
in the future (or perhaps is never accessed again). But that requires
knowing the future…
[CLICK] Here’s an idea: let’s predict future accesses by looking a
recent accesses and applying the principle of locality. If a line
has not been recently accessed, it’s less likely to be accessed in the
near future.
[CLICK] That suggests the least-recently-used replacement strategy,
usually referred to as LRU: replace the line that was accessed
furthest in the past. LRU works well in practice, but requires us to
keep a list ordered by last use for each set of cache lines, which
would need to be updated on each cache access. When we needed to
choose which member of a set to replace, we’d choose the last cache
line on this list. For an 8-way SA cache there are 8! possible
orderings, so we’d need log2(8!) = 16 state bits to encode the current
ordering. The logic to update these state bits on each access isn’t
cheap; basically you need a lookup table to map the current 16-bit
value to the next 16-bit value. So most caches implement an
approximation to LRU where the update function is much simpler to
compute.
[CLICK] There are other possible replacement policies: First-in,
first-out, where the oldest cache line is replaced regardless of when
it was last accessed. And Random, where some sort of pseudo-random
number generator is used to select the replacement.
All replacement strategies except for random can be defeated. If you
know a cache’s replacement strategy you can design a program that will
have an abysmal hit rate by accessing addresses you know the cache
just replaced. I’m not sure I care about how well a program designed
to get bad performance runs on my system, but the point is that most
replacement strategies will occasionally cause a particular program to
execute much more slowly than expected.
When all is said and done, an LRU replacement strategy or a close
approximation is a reasonable choice.

## Slide 32: Cache Evaluation
Cache designs have many parameters:
  Cache size in bytes
  Number of ways, the degree of associativity
  Number of outstanding requests (coming)
  Replacement policy
  Line size, i.e., the number of words in a line
A typical method of evaluating performance is by calculating the number of cache hits for a given set of cache parameters and a give set of memory reference sequences
  Memory reference sequences are generated by simulating program execution
  Number of hits, though fixed for a given memory reference pattern and cache design parameters, is extremely tedious to calculate (so it is done using a cache simulator)
~Decreasing order of importance

## Slide 33: Blocking vs. Non-Blocking cache
Blocking cache
  At most one outstanding miss
  Cache must wait for memory to respond
  Cache does not accept processor requests in the meantime
Non-blocking cache
  Continuous processing of cache hits
  Blocks processing in case N outstanding misses
Non-blocking caches are much harder to design but also give much better performance
Complications: out of order responses; internal pipelining in tag and data accesses, …

## Slide 34: Modular Cache Design
A useful abstraction reusable to build different caches

## Slide 35: Cache Organization Another design abstraction
req
resp
lineReq
lineResp
lineReqQ
lineRespQ
state
cache-array unit (cau) encapsulates data, tag and status arrays, which are all made from SRAM
Need queues to communicate with the back-end memory
hitQ holds the responses until the processor picks them up
state and current req registers hold the request and its status while the request is being processed
current reqQ
cache-array unit
hitQ
cau current reqQ
Notes: Miss Status Handling Registers (states)

## Slide 36: Cache-Array Unit Functionality
Suppose a request gets a hit in the cache-array unit
  Load hit returns a word
  Store hits returns nothing (void)
In case of a miss, the line slot must have been occupied; all the data in the missed slot is returned so that it can be written to the back-end memory if necessary
When the correct data becomes available from the back- end memory, the cache-array line is updated
req
resp
cache-array unit
update
cau current reqQ

## Slide 37: Cache-Array Unit Interface
interface CAU#(numeric type logNLines);
method Action req(MemReq r);
method ActionValue#(CAUResp) resp();
method Action update(CacheIndex index, TaggedLine newline);
endinterface
typedef struct{HitMissType hitMiss; Word ldValue;
TaggedLine taggedLine;} CAUResp;
typedef enum{LdHit, StHit, Miss} hitMiss;
typedef struct{Line line; CacheStatus status; CacheTag tag;
} TaggedLine;
req
resp
cache-array unit
update
cau current reqQ
Notes: Assume that the maximum value of logNLines is 10, giving us a maximum CAU of 64K bytes. Assume all CAU address sizes are 10bits regardless of the value of logNLines. This way we can avoid parameterizing CAU methods by logNLines
defined in CacheTypes.bsv

## Slide 38: Cache with non-blocking hits
module mkNonBlockingCache(Cache#(LogNLines));
CAU#(LogNLines) cau <- mkCAU();
FIFO#(Word) hitQ <- mkBypassFIFO;
FIFO#(MemReq) currReqQ <- mkPipelineFIFO;
Reg#(ReqStatus) state <- mkReg(WaitCAUResp);
FIFO#(LReq) lineReqQ <- mkFIFO;
FIFO#(Line) lineRespQ <- mkFIFO;
method Action req(MemReq req) ... method ActionValue#(Word) resp() ...
method ActionValue#(LReq) lineReq ... method Action lineResp(Line r) ...
endmodule
Rule to process CAU Response
Rule to send a LineReq to DRAM
Rule to process a LineResp from DRAM
WaitCAUResp ->
(if miss SendReq -> WaitDramResp) -> WaitCAUResp
State Elements
Notes: Rules to process a request including cache misses
Ready -> WaitCAUResp ->
(if miss then (SendReq -> WaitDramResp)) -> Ready

## Slide 39: non-blocking hits methods
method Action req(MemReq r);
cau.req(r);
currReqQ.enq(r);
endmethod
method ActionValue#(Word) resp;
hitQ.deq(); return hitQ.first;
endmethod
method ActionValue#(LReq) lineReq();
lineReqQ.deq(); return lineReqQ.first();
endmethod
method Action lineResp (Line r);
lineRespQ.enq(r);
endmethod

## Slide 40: cache-array unit
module mkCAU(CAU#(LogNLines));
Instantiate SRAMs for dataArray, tagArray, statusArray;
Reg#(CAUStatus) status <- mkReg(Ready);
Reg#(MemReq) currReq <- mkRegU; //shadow of outer currReq
method Action req(MemReq r);
initiate reads to tagArray, dataArray, and statusArray;
store request r in currReq
endmethod
method ActionValue#(CAUResp) resp;
Wait for responses for earlier requests
Get currTag, idx, wOffset from currReq.addr and do tag match
In case of a Ld hit, return the word; St hit, update the word;
In case of a miss, return the data, tag and status;
endmethod
method Action update(CacheIndex index, TaggedLine newline);
update the SRAM arrays at index
endmethod
endmodule
req
resp
cache-array unit
update

## Slide 41: non-blocking hits cache rules rule waitCAUResponse
rule waitCAUResponse (state == WaitCAUResp);
let x <- cau.resp; let currReq = currReqQ.first;
case (x.hitMiss)
LdHit :
StHit :
Miss : begin let oldTaggedLine = x.taggedLine;
extract cstatus, evictLaddr, line from oldTaggedLine
if the line is Dirty // writeback required
Store the line in DRAM;
state<= SendReq;
else // no writeback required
extract newLaddr from currReq
Request the line from DRAM;
state <= WaitDramResp;
end
endcase
endrule
begin Word v = x.ldValue;
hitQ.enq(v); currReqQ.deq; end
currReqQ.deq;
Notes: rule sendReq if (state == SendReq);
let newLaddr = {getTa
lineReqQ.enq(Lreq{op: Ld, laddr: newLaddr, line: ?}
state <= WaitDRAMResp;
endrule

## Slide 42: Blocking cache rules rule waitDramResponse
rule waitDramResponse(state == WaitDramResp);
let line = lineRespQ.first(); lineRespQ.deq();
let currReq = currReq.first; currReq.deq;
get idx, tag, wOffset from currReq.addr;
if currReq is Ld
put the response in hitQ;
update cau;
else St
update the word in the line
update cau
state <= WaitCAUResp;
endrule

## Slide 43: Summary?

## Slide 44: Write Through Caches
L1 values are always consistent with values in the next level cache 
No need for dirty array
No need to write back on evacuation

## Slide 45: L1+Store Buffer (write-through, write-miss-no-allocate): Req method
method Action req(MemReq r) if(mshr == Ready);
... get idx, tag and wOffset
if (request is a Ld) // search stb
x = stb.search(r.addr);
if (x is valid) then enque x in hitQ;
else // search L1
if (hit) then
enqueue the appropriate word in hitQ;
else missReq <= r; mshr <= StartMiss;
else // the request is a St
enqueue <addr, data> in stb
endmethod
No change

## Slide 46: Start-miss and Send-fill rules (write-through)
rule startMiss(mshr == StartMiss);
extract idx from missing address;
extract tag from tagArray;
extract dirty bit from dirtyArray;
if tag is valid and line is dirty // write-back
enque a store request for the dirty line in memReqQ;
mshr <= SendFillReq;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule sendFillReq (mshr == SendFillReq);
memReqQ.enq(missReq); mshr <= WaitFillResp;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
No need for this rule – miss can directly go into SendFillReq state

## Slide 47: Wait-fill rule (write-through)
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule waitFillResp(mshr == WaitFillResp);
extract idx and tag from miss request addr;
let data be the first element in memRespQ;
update tagArray;
if (miss request is Ld) then
update dataArray; enque word in hitQ
// no dirty array to update;
else // miss request is a St
update the line
update dataArray;
memRespQ.deq; mshr <= Ready;
endrule
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 48: Miss rules (cleaned up)
Ready -> SendFillReq -> WaitFillResp -> Ready
rule waitFillResp(mshr == WaitFillResp);
extract idx and tag from missing address;
Let data be the first element in memRespQ
update tagArray and dataArray
enqueue appropriate word in hitQ;
endrule
rule sendFillReq (mshr == SendFillReq);
memReqQ.enq(missReq); mshr <= WaitFillResp;
endrule
Ready -> SendFillReq -> WaitFillResp -> Ready
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 49: Exit from Store Buff (write-through, write-miss-no-allocate)
rule mvStbToL1 (mshr == Ready);
Extract idx, tag and wOffset
memReqQ.enq(...) // always send store to memory
let the first entry in stb be <addr,data>;
move this entry into L1 if address is present in L1
else
missReq <= r; mshr <= StartMiss;
endrule