## Slide 1
Complex Pipelining:
Out-of-Order Execution & Register Renaming
Arvind
Electrical Engineering and Computer Science
M.I.T.
Based on 6.823 lectures from 2005

## Slide 2: Complex Pipelining: Motivation
Pipelining becomes complex when we want high performance in the presence of
  Long latency or partially pipelined floating-point units
  Multiple function and memory units
  Memory systems with variable access time

## Slide 3: Function Unit Characteristics
fully
pipelined
partially
pipelined
Function units have internal pipeline registers
   operands are latched when an instruction
    enters a function unit
   inputs to a function unit (e.g., register file)
  can change during a long latency operation
busy
1cyc
1cyc
1cyc
accept
busy
2 cyc
2 cyc
accept

## Slide 4: Improving Memory Performance
separate instruction and data memory ports
     no self-modifying code
caches
    single cycle except in case of a miss stall
interleaved memory
    multiple memory accesses  bank conflicts
split-phase memory operations
     out-of-order responses

## Slide 5: Complex Pipeline Structure (abstract view)
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s

## Slide 6: Complex Pipeline Control Issues
Structural conflicts at the writeback stage due to
variable latencies of different function units
Structural conflicts at the execution stage if some
FPU or memory unit is not pipelined and takes
more than one cycle
Out-of-order write hazards due to variable
latencies of different function units
How to handle exceptions?

## Slide 7: Complex In-Order Pipeline
Delay writeback so all operations have the same latency to W stage
Avoid oversubscribing Write ports
Use bypassing on single-cycle integer operations to mitigate increased writeback latency
Superscalar execution
Commit Point
PC
Inst. Mem
D
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
Fadd
X3
X3
FPRs
X1
X2
Fmul
X3
X2
FDiv
X3
Unpipelined divider

## Slide 8: Need to understand Dependence Analysis in order to understand OOO execution

## Slide 9: Types of Data Hazards
Consider executing a sequence of
rk (ri) op (rj)
type of instructions
Data-dependence
      r3  (r1) op (r2) Read-after-Write
      r5  (r3) op (r4) (RAW) hazard
Anti-dependence
      r3  (r1) op (r2) Write-after-Read
      r1  (r4) op (r5) (WAR) hazard
Output-dependence
      r3  (r1) op (r2) Write-after-Write
      r3  (r6) op (r7) (WAW) hazard

## Slide 10: Detecting Data Hazards
Range and Domain of instruction i
    R(i) = Registers (or other storage) modified by
    instruction i
    D(i) = Registers (or other storage) read by
        instruction i
Suppose instruction j follows instruction i in the
program order. Executing instruction j before the
effect of instruction i has taken place can cause a
    RAW hazard if R(i)  D(j) 
    WAR hazard if D(i)  R(j) 
    WAW hazard if R(i)  R(j) 

## Slide 11: Register vs. Memory Data Dependence
Data hazards due to register operands can be
determined at the decode stage but
data hazards due to memory operands can be
determined only after computing the effective
address
    store M[(r1) + disp1]  (r2)
    load r3  M[(r4) + disp2]
    Does (r1 + disp1) = (r4 + disp2) ?

## Slide 12: Data Hazards: An Example
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
RAW Hazards
WAR Hazards
WAW Hazards

## Slide 13: Instruction Scheduling
I6
I2
I4
I1
I5
I3
Valid orderings:
in-order I1 I2 I3 I4 I5 I6
out-of-order
out-of-order
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
I2 I1 I3 I4 I5 I6
I1 I2 I3 I5 I4 I6

## Slide 14: Out-of-order Completion In-order Issue
Latency
I1 DIVD f6, f6, f4 4
I2 LD f2, 45(r3) 1
I3 MULTD f0, f2, f4 3
I4 DIVD f8, f6, f2 4
I5 SUBD f10, f0, f6 1
I6 ADDD f6, f8, f2 1
in-order comp 1 2
out-of-order comp 1 2
1 2 3 4 3 5 4 6 5 6
2 3 1 4 3 5 5 4 6 6

## Slide 15
Scoreboard: A Hardware Data Structure to Detect Hazards Dynamically

## Slide 16: CDC 6600 Seymour Cray, 1963
A fast pipelined machine with 60-bit words
  128 Kword main memory capacity, 32 banks
Ten functional units (parallel, unpipelined)
  Floating Point: adder, 2 multipliers, divider
  Integer: adder, 2 incrementers, ...
Hardwired control (no microcoding)
Dynamic scheduling of instructions using a scoreboard
Ten Peripheral Processors for Input/Output
  a fast multi-threaded 12-bit integer ALU
Very fast clock, 10 MHz (FP add in 4 clocks)
>400,000 transistors, 750 sq. ft., 5 tons, 150 kW, novel freon-based technology for cooling
Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)

## Slide 17: IBM Memo on CDC6600
Thomas Watson Jr., IBM CEO, August 1963:
  “Last week, Control Data ... announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers... Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world's most powerful computer.”
To which Cray replied: “It seems like Mr. Watson has answered his own question.”

## Slide 18: Complex Pipeline
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s
Can we solve write hazards without equalizing all pipeline depths and without bypassing?

## Slide 19: When is it Safe to Issue an Instruction?
The following checks need to be made before the Issue stage can dispatch an instruction
  Is the required function unit available?
  Is the input data available?  RAW?
  Is it safe to write the destination? WAR? WAW?
  Is there a structural conflict at the WB stage?
Design a data structure to keep track of all the instructions in all the functional units

## Slide 20: A Data Structure for Correct Issues Keeps track of the status of Functional Units
The instruction i at the Issue stage consults this table
  FU available? check the busy column
  RAW? search the dest column for i’s sources
  WAR? search the source columns for i’s destination
  WAW? search the dest column for i’s destination
An entry is added to the table if no hazard is detected;
An entry is removed from the table after Write-Back
Name Busy Op Dest Src1 Src2
  Int
  Mem
  Add1
  Add2
  Add3
  Mult1
  Mult2
  Div

## Slide 21: Simplifying the Data Structure Assuming In-order Issue
Suppose the instruction is not dispatched by the Issue stage if a RAW hazard exists or the required FU is busy, and that operands are latched by functional unit on issue:
  Can the dispatched instruction cause a
    WAR hazard ?
    WAW hazard ?
NO: Operands read at issue
YES: Out-of-order completion
Notes:   Can the dispatched instruction cause a
    WAR hazard ? NO: Operands read at issue
    WAW hazard ? YES: Out-of-order completion

## Slide 22: Simplifying the Data Structure ...
No WAR hazard
 no need to keep src1 and src2
The Issue stage does not dispatch an instruction in
case of a WAW hazard
a register name can occur at most once in the
  dest column
WP[reg#] : a bit-vector to record the registers for which writes are pending
These bits are set to true by the Issue stage and
set to false by the WB stage
 Each pipeline stage in the FU's must carry the
  dest field and a flag to indicate if it is valid
  “the (we, ws) pair”

## Slide 23: Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
        (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set to true by the Issue stage and set to false by the WB stage
Issue checks the instruction (opcode dest src1 src2)
against the scoreboard (Busy & WP) to dispatch
    FU available?
    RAW?
    WAR?
    WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 24: Scoreboard Dynamics
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
  Functional Unit Status Registers Reserved
  Int(1) Add(1) Mult(3) Div(4) WB for Writes
t0 I1 f6 f6
t1 I2 f2 f6 f6, f2
t2 f6 f2 f6, f2 I2
t3 I3 f0 f6 f6, f0
t4 f0 f6 f6, f0 I1
t5 I4 f0 f8 f0, f8
t6 f8 f0 f0, f8 I3
t7 I5 f10 f8 f8, f10
t8 f8 f10 f8, f10 I5
t9 f8 f8 I4
t10 I6 f6 f6
t11 f6 f6 I6

## Slide 25: In-Order Issue Pipeline
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s

## Slide 26: Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
        (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set to true by the Issue stage and set to false by the WB stage
Issue checks the instruction (opcode dest src1 src2)
against the scoreboard (Busy & WP) to dispatch
    FU available?
    RAW?
    WAR?
    WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 27: In-Order Issue Limitations: an example
latency
1 LD F2, 34(R2) 1
2 LD F4, 45(R3) long
3 MULTD F6, F4, F2 3
4 SUBD F8, F2, F2 1
5 DIVD F4, F2, F8 4
6 ADDD F10, F6, F4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
In-order restriction prevents instruction 4 from being dispatched

## Slide 28: Out-of-Order Issue
Issue stage buffer holds multiple instructions waiting to issue.
Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
Any instruction in buffer whose RAW hazards are satisfied can be issued (for now at most one dispatch per cycle). On a write back (WB), new instructions may get enabled.
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 29: In-Order Issue Limitations: an example
latency
1 LD F2, 34(R2) 1
2 LD F4, 45(R3) long
3 MULTD F6, F4, F2 3
4 SUBD F8, F2, F2 1
5 DIVD F4, F2, F8 4
6 ADDD F10, F6, F4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
Out-of-order: 1 (2,1) 4 4 . . . . 2 3 . . 3 5 . . . 5 6 6
Out-of-order execution did not allow any significant improvement!

## Slide 30: How many Instructions can be in the pipeline
Which features of an ISA limit the number of
instructions in the pipeline?
Which features of a program limit the number of
instructions in the pipeline?
Out-of-order dispatch by itself does not provide any significant performance improvement !
Number of Registers
Control transfers

## Slide 31: Overcoming the Lack of Register Names
Floating Point pipelines often cannot be kept filled with small number of registers.
IBM 360 had only 4 Floating Point Registers
Can a microarchitecture use more registers than
specified by the ISA without loss of ISA compatibility ?
    Robert Tomasulo of IBM suggested an ingenious solution in 1967 based on on-the-fly register renaming

## Slide 32: Instruction-Level Parallelism with Renaming
latency
1 LD F2, 34(R2) 1
2 LD F4, 45(R3) long
3 MULTD F6, F4, F2 3
4 SUBD F8, F2, F2 1
5 DIVD F4’, F2, F8 4
6 ADDD F10, F6, F4’ 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
Out-of-order: 1 (2,1) 4 4 5 . . . 2 (3,5) 3 6 6
1
2
3
4
5
6
X
Any antidependence can be eliminated by renaming.
    (renaming  additional storage)
    Can it be done in hardware?
yes!

## Slide 33: Register Renaming
Decode does register renaming and adds instructions to the issue stage reorder buffer (ROB)
 renaming makes WAR or WAW hazards
impossible
Any instruction in ROB whose RAW hazards have been satisfied can be dispatched.
 Out-of-order or dataflow execution
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 34: Renaming & Out-of-order Issue An example
When are names in sources
replaced by data?
When can a name be reused?
1 LD F2, 34(R2)
2 LD F4, 45(R3)
3 MULTD F6, F4, F2
4 SUBD F8, F2, F2
5 DIVD F4, F2, F8
6 ADDD F10, F6, F4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
.
data / ti
p data
F1
F2
F3
F4
F5
F6
F7
F8
Whenever an FU produces data
Whenever an instruction completes

## Slide 35: Data-Driven Execution
Renaming
table &
reg file
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the
Decode stage, which also stores the tag in the reg file
When an instruction completes, its tag is deallocated
Replacing the
tag by its value
is an expensive
operation

## Slide 36: Dataflow execution
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are availble (p1 and p2 are set)
Reorder buffer
t1
t2
.
.
.
tn
ptr2
next to
deallocate
prt1
next
available
Ins# use exec op p1 src1 p2 src2

## Slide 37: Simplifying Allocation/Deallocation
Instruction buffer is managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free
Reorder buffer
t1
t2
.
.
.
tn
ptr2
next to
deallocate
prt1
next
available
Ins# use exec op p1 src1 p2 src2

## Slide 38: IBM 360/91 Floating Point Unit R. M. Tomasulo, 1967
Mult
p
data
p
data
1
2
p
data
1
2
3
4
5
6
data
load
buffers
(from
memory)
1
2
3
4
Adder
p
data
p
data
1
2
3
Floating
Point
Reg
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it
distribute
instruction
templates
by
functional
units
< t, result >
p
data

## Slide 39: Effectiveness?
Renaming and Out-of-order execution was first
implemented in 1969 in IBM 360/91 but did not show up in the subsequent models until mid-Nineties.
Why ?
Reasons
    1. Exceptions not precise!
    2. Effective on a very small class of programs
    One more problem needed to be solved
Control transfers

## Slide 40: Precise Interrupts
It must appear as if an interrupt is taken between two instructions (say Ii and Ii+1)
  the effect of all instructions up to and including Ii is
  totally complete
  no effect of any instruction after Ii has taken place
The interrupt handler either aborts the program or
restarts it at Ii+1 .

## Slide 41: Effect on Interrupts Out-of-order Completion
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
out-of-order comp 1 2 2 3 1 4 3 5 5 4 6 6
restore f2 restore f10
Consider interrupts
Precise interrupts are difficult to implement at high speed
- want to start execution of later instructions before
exception checks finished on earlier instructions

## Slide 42: In-Order Commit for Precise Exceptions
Instructions fetched and decoded into instruction
reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile &
memory, is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Kill
Kill
Kill
Exception?
Inject handler PC

## Slide 43: Extensions for Precise Exceptions
Reorder buffer
ptr2
next to
commit
ptr1
next
available
add <pd, dest, data, cause> fields in the instruction template
commit instructions to reg file and memory in program
order  buffers can be maintained circularly
on exception, clear reorder buffer by resetting ptr1=ptr2
(stores must wait for commit before updating memory)
Inst# use exec op p1 src1 p2 src2 pd dest data cause

## Slide 44: Rollback and Renaming
Register file does not contain renaming tags anymore.
How does the decode stage find the tag of a source register?
Search the “dest” field in the reorder buffer
Register File
(now holds only committed state)
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit

## Slide 45: Renaming Table
Register File
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
Renaming table is a cache to speed up register name look up. It needs to be cleared after each exception taken.
When else are valid bits cleared?
Control transfers
r1
t
v
r2
tag
valid bit

## Slide 46
Summary

## Slide 47: Phases of Instruction Execution
Fetch: Instruction bits retrieved from cache.
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute: Instructions and operands sent to execution units .
When execution completes, all results and exception flags are available.
Decode: Instructions placed in appropriate issue (aka “dispatch”) stage buffer
Result
Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation” or “completion”).
PC

## Slide 48: Fetch Stage
PC
Instruction Cache
Hit?
Instructions
To Decode Stage
Fetch Buffer
Opcode
Rd
Rsrc1
Rsrc2/Imm

## Slide 49: Decode & Rename Stage
Opcode
Rd
Rsrc1
Rsrc2/Imm
Opcode
U
E
Tag1
P1
Data1
Tag2
P2
Data2
Rd
Pd
Datad
Cause
t1
t2
tn
0 1
0 1
1
ImmSel
0 1
0 1
0 1
Tag
V
Tag
V
Tag
V
Rename Table
R0
R30
R31
1
X
SignExt
R0
R30
R31
Committed Architectural Regfile
(Renaming is shown only for Rsrc2, similar for Rsrc1)
ROB

## Slide 50: Execute Stage
Func. Unit
Opcode
U
E
Tag1
P1
Data1
Tag2
P2
Data2
Rd
Pd
Datad
Cause
Opcode
U
E
Tag1
P1
Data1
Tag2
P2
Data2
Rd
Pd
Datad
Cause
t1
t2
tn
ROB
Arbiter selects one ready instruction (P1=1 AND P2=1) to execute
Instruction reads operands from ROB, executes, and broadcasts tag and result to waiting instructions in ROB. Also saves result and exception flags for commit.

## Slide 51: Commit Stage
tn
Tag
V
Tag
V
Tag
V
Rename Table
R0
R30
R31
R0
R30
R31
Committed Architectural Regfile
Exception?
=?
Clear rename valid?
Opcode
U
E
Tag1
P1
Data1
Tag2
P2
Data2
Rd
Pd
Datad
Cause
t1
ptr2
ROB
When instruction at ptr2 (commit point) has completed, write back result to architectural state and check for exceptions
Check if rename table entry for architectural register written matches tag, if so, clear valid bit in rename table

## Slide 52
Many optimizations are needed before an OOO architecture becomes profitable.
Thank you !