## Slide 1
Constructive Computer Architecture
Multithreaded Programming:
Synchronization and
Sequential Consistency
Tushar Krishna (+ Arvind)
Electrical Engineering and Computer Science
Massachusetts Institute of Technology

## Slide 2: Recap: Threads
Code
Data
Code
Data
Code
Data
Code
Data
PCB
PCB
PCB
PCB
Thread
Process
PCB: Process Control Block
(PC, stack pointer, ..)
Running multiple threads concurrently on same CPU
Notes: How do you disambiguate between different threads.
Share code, share PC. .. Thread_id stored in a special control status register ..

## Slide 3: Example use of threads
compute
compute
I/O
I/O result
Needed
Sequential process
Compute
thread
I/O result
Needed
I/O request
I/O complete
I/O
thread
Multithreaded process
Digitizer
Tracker
Alarm
Producer-Consumer process
Slide Courtesy: GT CS 2200 (U. Ramachandran)

## Slide 4: Recap: Threads
Code
Data
Code
Data
Code
Data
Code
Data
PCB
PCB
PCB
PCB
Thread
Process
PCB: Process Control Block
(PC, stack pointer, ..)
Software
Hardware
CPU A
CPU B
CPU C
What is SMT?
Running multiple threads concurrently on same CPU
What is Multiprocessing?
Running multiple threads concurrently on same CPU
Running multiple threads concurrently over multiple CPUs
Notes: How do you disambiguate between different threads.
Share code, share PC. .. Thread_id stored in a special control status register ..

## Slide 5: Symmetric Multiprocessors
All memory is equally accessible to all processors
Any processor can do any I/O operation
Memory
Processor-Memory Interconnect
bridge
Processor
+ cache
I/O controller
Graphics
output
I/O controller
I/O controller
I/O Interconnect
Networks
Processor
+ cache
Notes: Shared Memory Abstraction
Case 1: same cores
Case 2: multiple cores.

## Slide 6: Heterogeneous Processors
In modern Systems-on-a-Chip (SoC) there are many processors to perform specific functions; they are programmed in an ad-hoc manner
Memory
Processor-Memory Interconnect
bridge
Processor
+ cache
Proc + Mem
Graphics
output
Proc + Mem
Proc + Mem
I/O Interconnect
Networks
Processor
+ cache
minions
Notes: [Maybe move it later?]

## Slide 7: Multithreaded Programming
Multiple independent sequential threads which compete for shared resources such as memory and I/O devices
  usually managed by the operating system
  OS often runs multiple threads for efficient management of resources even on a single processor
Multiple cooperating sequential threads, which communicate via the shared memory system, i.e., shared data structures
  an application can often be completed faster by decomposing it into multiple threads and running them on multiprocessors

## Slide 8: Focus of Today’s Lecture
Supporting Multi-threaded Programming
  Synchronization
  Sequential Consistency

## Slide 9: Focus of Today’s Lecture
Supporting Multi-threaded Programming
  Synchronization
  Sequential Consistency

## Slide 10: Synchronization
Need for synchronization arises whenever there are parallel processes or threads in a system
producer
consumer
fork
join
P1
P2
  Forks and Joins: A parallel process/thread may want to wait until several events have occurred
  Producer-Consumer: A consumer process/thread must wait until the producer process has produced data
  Mutual Exclusion: Operating system has to ensure that a resource is used by only one process/thread at a given time

## Slide 11: Thread-safe programming
Multithreaded programs can be executed on a uniprocessor by timesharing
  Each thread is executed for a while (timer interrupt) and then the OS switches to another thread, repeatedly
Thread-safe multithreaded programs behave the same way regardless of whether they are executed on multiprocessors or a single processor
In the rest of lecture we will assume that each thread has its own processor to run

## Slide 12: Example: Producer-Consumer communicate via a FIFO
Producer posting Item x:
Load Rtail, tail
Store (Rtail), x
Rtail=Rtail+1
Store tail, Rtail
Consumer:
Load Rhead, head
spin: Load Rtail, tail
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store head, Rhead
process(R)
Producer
Consumer
tail
head
Rtail
Rtail
Rhead
R
Assume unbounded FIFO
dest addr
src addr
dest addr
in a reg

## Slide 13: Multithreaded programming is subtle
Producer posting Item x:
Load Rtail, tail
Store (Rtail), x
Rtail’=Rtail+1
Store tail, Rtail’
Consumer:
Load Rhead, head
spin: Load Rtail, tail
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store head, Rhead
process(R)
Producer
Consumer
tail
head
Rtail
Rtail
Rhead
R
reordering the stores can cause the consumer to see stale data
Rtail’
What is wrong with this code?

## Slide 14: Multiple Consumers
Producer posting Item x:
Load Rtail, tail
Store (Rtail), x
Rtail=Rtail+1
Store tail, Rtail
Consumer:
Load Rhead, head
spin: Load Rtail, tail
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store head, Rhead
process(R)
What is wrong with this code?
tail
head
Producer
Rtail
Consumer
1
R
Rhead
Rtail
Consumer
2
R
Rhead
Rtail
The same item may get consumed by both consumers!
Critical section:
Needs to be executed atomically by one consumer  locks

## Slide 15: Locks or Semaphores E. W. Dijkstra, 1965
Lock s has two values:
  Unlocked (s=0): means that no process has the lock
  Locked (s=1): means that exactly one process has the lock and it can access the critical section
Once a process successfully acquires a lock, it executes the critical section and then sets s to zero by releasing the lock
The execution of the critical section is protected by locks; Only one process can hold the lock at a time
Process i
  acquire(s)
  <critical section>
  release(s)
Implementing locks is quite difficult; ISAs provide special atomic instructions to implement locks

## Slide 16: Atomic read-modify-write instructions
Test&Set m, R:
  R  M[m];
  if R==0 then
M[m] 1;
Swap m, R:
  Rt  M[m];
  M[m] R;
  R  Rt;
m is a memory location, R is a register
Location m can be set to one only if it contains a zero; the old value is returned in R
Location m is first read and then set to the new value; the old value is returned in R
Notes: Note: example of multi-thread programming: pthreads
It provides a function calls to lock, which is implemented via these instructions in the compiled code

## Slide 17: Multiple Consumers Example using the Test&Set Instruction
Critical
Section
lock: Test&Set mutex, Rtemp
if (Rtemp==1) goto lock
Load Rhead, head
spin: Load Rtail, tail
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store head, Rhead
unlock: Store mutex, 0
process(R)
A consumer acquires the lock (mutex) before reading the head value
Notes: If critical sections too large, leads to loss of concurrency

## Slide 18: Synchronization and Concurrency
T1 is active and executing code inside its critical section.
T2 is active and executing code outside its critical section.
T3 is active and executing code outside its critical section.
T4 is blocked and waiting to get into its critical section.
  (It will get in once the lock is released by T1).
Critical section
Critical section
Critical section
Critical section
T1
T2
T3
T4

## Slide 19: Programming Challenges
How to decide what part of code is the “critical section”?
  What happens if critical section is too large?
Our example was written assuming that the instructions per thread are executed in order
  An architecture may execute instructions out of order to gain higher performance
   Gives rise to memory model issues

## Slide 20: Implementation Challenges
Atomic instructions (read-modify-write) are quite disruptive in pipelined machines
What if the process stops or is swapped out while in the critical section?
  Lock may never get released! Every thing stops
  More sophisticated programming is needed to deal with such eventualities

## Slide 21: Focus of Today’s Lecture
Supporting Multi-threaded Programming
  Synchronization
  Sequential Consistency

## Slide 22: Memory Ordering Nuances
Concurrent tasks: T1, T2
Shared variables: X, Y (initially X = 0, Y = 0)
T1: T2:
  Store X, 1 (X = 1) Load R1, Y
  Store Y, 2 (Y = 2) Store Y’, R1 (Y’= Y)
  Load R2, X
  Store X’, R2 (X’= X)
What are the legitimate answers for X’ and Y’ ?
(X’,Y’)  {(1,2), (0,0), (1,0), (0,2)} ?
If y is 2 then x cannot be 0

## Slide 23: Sequential Consistency A Memory Model
“A system is sequentially consistent if the result of
any execution is the same as if the operations of all
the processors were executed in some sequential
order, and the operations of each individual processor
appear in the order specified by the program”
Leslie Lamport
Sequential Consistency =
arbitrary order-preserving interleaving
of memory references of sequential programs
M
P
P
P
P
P
P

## Slide 24: Why SC may be violated
Sequential consistency imposes more memory ordering constraints than those imposed by uniprocessor program dependencies ( )
What are these in our example ?
T1: T2:
  Store X, 1 (X = 1) Load R1, Y
  Store Y, 2 (Y = 2) Store Y’, R1 (Y’= Y)
  Load R2, X
  Store X’, R2 (X’= X)
additional SC requirements ( )
High-performance processor implementations often violate SC by not enforcing the extra dependencies required by SC
Example Store Buffers

## Slide 25: Store Buffers
A processor considers a Store to have been executed as soon as it is stored in the Store buffer, that is, before it is put in memory
A load can read values from the local store buffer (forwarding)
P
Memory
P
Loads/Stores can appear to be ordered differently to other processors
==> violate SC
Some systems only enforce FIFO ordering for the stores to the same address while
moving a store from store buffer to memory
Notes: In LSQ, the Store Queue can be rolled back.
Store Buffer is committed stores on the way to memory.
Clarify “Store Buffer” here different from the one in the lab.

## Slide 26: Violations of SC Example 1
Sequential consistency:
With FIFO store buffers:
With non-FIFO store buffers:
Process 1 Process 2
Store X, 1; Load R1, Y; Store Y, 2; Load R2, X;
Question: Is it possible that R1=2 but R2=0?
No
No
Yes
Initially, all memory
locations contain zeros

## Slide 27: Violations of SC Example 2
Sequential consistency:
Suppose Stores don’t leave the store buffers before the Loads are executed:
Process 1 Process 2
Store X, 1; Store Y, 2;
Load R1, Y; Load R2, X;
Initially, all memory
locations contain zeros
Question: Is it possible that R1=0 and R2=0?
No
Yes !

## Slide 28: A Practical Producer-Consumer Example continued
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
Rtail=Rtail+1
Store tail, Rtail
Consumer:
Load Rhead, head
spin: Load Rtail, tail
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store head, Rhead
process(R)
Can the tail pointer get updated
before the item x is stored?
Programmer assumes that if 3 happens after 2, then 4 happens after 1.
Problem sequences:
  2, 3, 4, 1
  4, 1, 2, 3
1
2
3
4
How do we determine which sequences are allowed?
Notes: Subtle question – what does ‘store completion’ really mean?

## Slide 29: Memory Consistency Model
In practice, processors use “weaker” memory models than SC
  Why?
The “Memory Consistency Model” (aka Memory Model) describes what values can be returned by load instructions across concurrent processes/threads

## Slide 30: TSO: A memory model for machines with store buffers
A store first goes into the Store buffer (SB)
A load reads the youngest corresponding entry from SB before reading the memory
A store is dequeued from the SB in FIFO order to update the monolithic memory (background rule)
A commit fence stalls local execution until SB is empty
Monolithic memory
…
Processor
Reg state
Processor
Reg state
Store
buffer
Store
buffer
simple and vendor independent
St a v
<a,v>
<a,v>
TSO allows loads to overtake stores
Notes: Monolithic Memory is the memory hierarchy (L1, L2, ..)

## Slide 31: Memory Fences Instructions to sequentialize memory accesses
Processors which do not support SC memory model provide memory fence instructions to force the serialization of memory accesses as needed
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
FenceSS
Rtail=Rtail+1
Store tail, Rtail
Consumer:
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
FenceLL
Load R, (Rhead)
Rhead=Rhead+1
Store head, Rhead
process(R)
ensures that tail ptr
is not updated before
x has been stored
ensures that R is
not loaded before
x has been stored
RISC-V has one instruction called “fence”

## Slide 32: Memory Model Challenges
Architectural optimizations that are correct for uniprocessors, often violate sequential consistency and result in a new memory model for multiprocessors
Memory model issues are subtle and contentious
  x86 ISA uses TSO, whose definition is easy to understand and unambiguous
  ISAs for ARM, PowerPC etc. use weaker memory models and even experts don’t agree on their definitions

## Slide 33: SC and Caches
Caches present a similar problem as store buffers – stores in one cache will not be visible to other caches automatically
Cache problem is solved differently – caches are kept coherent
P
Cache
Memory
P
Cache
How to build coherent caches is the topic of next lecture