## Slide 1
Constructive Computer Architecture
Cache Coherence
Tushar Krishna (+ Arvind)
Electrical Engineering and Computer Science
Massachusetts Institute of Technology

## Slide 2: SC and caches
Caches present a similar problem as store buffers – stores in one cache will not be visible to other caches automatically
Cache problem is solved differently – caches are kept coherent
P
Cache
Memory
P
Cache
How to build coherent caches is the topic of this lecture

## Slide 3: Cache-coherence problem
Suppose P1 updates A to 200.
  write-back: memory and cache-2 have stale values
  write-through: cache-2 has a stale value
cache-1
A 100
Processor-Memory Interconnect
P1
P2
cache-2
A 100
memory
A 100
200
200
Do these stale values matter for programming?
Yes, if we want to implement SC or, in fact, any reasonable memory model
Notes: Discuss:
What happens if P2 does a write.
How to keep data coherent?

## Slide 4: Shared Memory Systems
M
L1
P
L1
P
L1
P
L1
P
L2
L2
L1
P
L1
P
Interconnect
Modern systems often have hierarchical caches
Each cache has exactly one parent but can have zero or more children
Logically only a parent and its children can communicate directly
Inclusion property is maintained between a parent and its children, i.e.,
a  Li  a  Li+1
Because usually
Li+1 >> Li

## Slide 5: Cache-Coherent Memory
A monolithic memory processes one request at a time; it can be viewed as processing requests instantaneously
A memory with hierarchy of caches is said to be coherent, if functionally it behaves like the monolithic memory
req
res
req
res
Monolithic Memory
...

## Slide 6: Maintaining Coherence
In a coherent memory all loads and stores can be placed in a global order
  multiple copies of an address in various caches can cause this property to be violated
This property can be ensured if:
  Only one cache at a time has the write permission for an address
  No cache can have access to a stale copy of the data after a write to the address has been performed
      cache coherence protocols are used
      to maintain coherence

## Slide 7: Cache Coherence Protocols
Write request:
  the address is invalidated in all other caches before the write is performed
Read request:
  if a dirty copy is found in some other cache, then that value is written back to the memory and supplied to the reader. Alternatively, the dirty value can be forwarded directly to the reader
Such protocols are called Invalidation-based

## Slide 8: State and actions needed to maintain Cache Coherence
Each line in each cache maintains MSI state:
I - cache doesn’t contain the address
  S- cache has the address but so may other caches; hence it can only be read
  M- only this cache has the address; hence it can be read and written
S
M
I
store
load
write-back
invalidate
flush
store
Action on a read miss (i.e., Cache state is I):
  If some other cache has the address in state M then write back the dirty data to Memory and set its state to S
  Read the value from Memory and set the state to S
Action on a write miss (i.e., Cache state is I or S):
  Invalidate the address in other caches; in case some cache has the address in state M then write back the dirty data
  Read the value from Memory if necessary and set the state to M
How do we know the state of other caches?

## Slide 9: State ordering to develop protocols
S
M
I
store
load
write-back
invalidate
flush
store
The states M, S, I can be thought of as an order M>S>I
  Upgrade: A cache miss causes transition from a lower state to a higher state
  Downgrade: A write-back or invalidation causes a transition from a higher state to a lower state
    Voluntary Downgrade: Eviction (aka flush) due to lack of space

## Slide 10: Protocols are distributed! Fundamental assumptions
A processor or cache can only examine or set its own state
The state of other caches is inferred or set by sending request and response messages
Each parent cache maintains information about each of its child caches in a directory
  Directory information is conservative, e.g., if the directory say that the child cache c has a cache-line in state S, then cache c may have the address in either S or I state but not in M state
  Sometimes the state of a cache line is transient because it has requested a change. Directory also contains information about outstanding messages

## Slide 11: Directory State Encoding Two-level (L1, M) system
M
directory for a
Interconnect
<[S, no],I,[S, no],I>
P
L1
P
L1
P
L1
P
L1
P
[S,a]
[S,a]
a
Addr
Tag
Data Block
V
M/S
dir
<[(M|S|I), (No | Yes)]>
Child’s state
Waiting for downgrade response
for each child
-L1 has no directory
-Memory M has no need for state MSI

## Slide 12: Coherence Messages an abstract view
interconnect
PP
P
c2m
m2c
L1
p2m
m2p
M
PP
in
out
PP
P
c2m
m2c
L1
p2m
m2p
Each cache has 2 pairs of queues
  (c2m, m2c) to communicate with the memory
  (p2m, m2p) to communicate with the processor
Message format: <cmd, srcdst, a, s, data>
FIFO message passing between each (srcdst) pair except a Req cannot block a Resp
Messages in one srcdst path cannot block messages in another srcdst path
Req/Resp
address
state
PP: Protocol Processor
Notes: PP: Parent Protocol Processor.

## Slide 13: Coherence Messages an abstract view
Upgrade Req
L1
M
c2m
m2c
interconnect
c2m
m2c
Dngrade Resp
Upgrade Resp
Dngrade Req
Notes: Show an example.
I – I – I
S - I - I
S – I – S
M – I – I
S – S – I

## Slide 14: Network Requirements
Upgrade Req
c2m
m2c
interconnect
c2m
m2c
Dngrade Resp
Upgrade Resp
Dngrade Req
The interconnect has to emulate three independent virtual networks (vnet) to support the requirements of cache coherence protocols.
   Messages in one vnet cannot block messages in another vnet.
  Two FIFOs guarantee that an upgrade request cannot block a response message
  A downgrade request always completes and therefore it can share the same FIFO as for response messages
child
parent
   The same idea extends across a hierarchy of cache-levels

## Slide 15: Protocol Implementation
It never makes sense to have two outstanding requests for the same address from the same processor/cache
It is possible to have multiple requests for the same address from different processors. Hence there is a need to arbitrate requests
A cache needs to be able to evict an address in order to make room for a different address
  Voluntary downgrade
Memory system (higher-level cache) should be able to force a lower-level cache to downgrade
  caches need to keep track of the state of their children’s caches

## Slide 16: Consequences of distributed protocol
In a single cache system, a cache could go to sleep after it issues a request for a missing line
However, in a multicache system, a cache may receive an invalidation request at any time from other caches (via its parent); such requests cannot be ignored otherwise the system will deadlock
  none of the requests may be able to complete
A difficult part of the protocol design is to determine which request can arrive in a given state

## Slide 17: Example: CC protocol implementation for blocking caches

## Slide 18: Scenarios to be handled
1 Up-req send (cache)
2 Up-req proc, Up resp send (memory)
3 Up-resp proc (cache)
4 Dn-req send (memory)
5 Dn-req proc, Dn resp send (cache)
6 Dn-resp proc (memory)
7 Dn-req proc, drop (cache)
8 Voluntary Dn-resp (cache)
Cache
Memory
Cache
1
2
4
3
6
5
7
8

## Slide 19: Req method Hit processing
method Action req(MemReq r) if(mshr == Ready);
extract a and op from r;
if(a is a hit) begin
if(op is Ld)
hitQ.enq(data from dataArry);
else // op is St
if (state is M)
update dataArray;
else missReq <= r; // state is S
mshr <= SendFillReq;
missSlot <= slot;
else missReq <= r; // state is I
mshr <= StartMiss;
endmethod
PP
P
c2m
m2c
L1
p2m
m2p

## Slide 20: Start-miss & Send-fill rules
rule startMiss(mshr == StartMiss);
find a victim slot;
if (the victim slot is not I) // write-back (Evacuate)
extract addr a, state s, data d from the victim slot;
mark victim slot I;
c2m.enq(<Resp, c->m, a, I, d>);
mshr <= SendFillReq; remember victim slot number;
endrule
Rdy -> StartMiss -> SndFillReq -> WaitFillResp -> Resp -> Rdy
rule sendFillReq (mshr == SendFillReq);
// must have a reserved slot to receive reply
let upg = (missReq.op == Ld)? S : M;
c2m.enq(<Req, c->m, missReq.addr, upg, - >);
mshr <= WaitFillResp;
endrule // 1
1 Up-req send (cache)

## Slide 21: Wait-fill & Proc Resp rule
rule waitFillResp ((mshr == WaitFillResp) &&&
(m2c.firstResp matches <Resp, m->c, .a, .cs, .d>));
let slot = missSlot;
dataArray[slot] <=
(missReq.op == Ld)? d : missReq.data;
state[slot] <= (cs, a);
m2c.deqResp;
mshr <= Resp;
endrule // (3)
Rdy -> StrtMiss -> SndFillReq -> WaitFillResp -> Resp -> Rdy
rule sendProc(mshr == Resp);
if(missReq.op == Ld) begin let slot = missSlot;
c2p.enq(dataArray[slot]); end
mshr <= Ready;
endrule
3 Up-resp process (cache)
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 22: Parent Responds
rule parentResp
(c2m.firstReq matches <Req,.c->m,.a,.y,.*>);
  let slot = getSlot(state, a); // in a 2-level
  // system a has to be present in the memory
  let statea = state[slot];
  if((i≠c, isCompatible(statea.dir[i],y))
  && (statea.waitc[c]=No)) begin
  let d =(statea.dir[c]=I)? dataArray[slot]: -);
  m2c.enq(<Resp, m->c, a, y, d>);
  state[slot].dir[c]:=y;
  c2m.deq;
  end
endrule // 2
IsCompatible(M, M) = False
IsCompatible(M, S) = False
IsCompatible(S, M) = False
All other cases = True
2 Up-req process, Up resp send (memory)

## Slide 23: Parent (Downgrade) Requests
rule dwn
(c2m.firstReq matches <Req,c->m,.a,.y,.*>);
let slot = getSlot(state, a);
  let statea = state[slot];
if (findChild2Dwn(statea) matches (Valid .i))
begin
state[slot].waitc[i] <= Yes;
m2c.enq(<Req, m->i, a, (y==M?I:S), ? >);
end;
endrule // (4)
This rule will execute as long some child cache is not compatible with the incoming request
4 Dn-req send (memory)

## Slide 24: Parent receives Response
rule dwnRsp
(c2m.firstResp matches <Resp, c->m, .a, .y, .data>);
c2m.deqResp;
let slot = getSlot(state, a);
  let statea = state[slot];
if(statea.dir[c]== M) dataArray[slot]<=data;
state[slot].dir[c]<=y;
state[slot].waitc[c]<=No;
endrule // (6)
6 Dn-resp process (memory)

## Slide 25: Child Responds Incoming downgrade requests in L1
rule dng ((mshr != Resp) &&&
(m2c.firstReq matches <Req,m->c,.a,.y,.*>);
let slot = getSlot(state,a);
if(getCacheState(state[slot])>y) begin
let d = (isStateM(state[slot])? dataArray[slot]: -);
c2m.enq(<Resp, c->m, a, y, d>);
state[slot] <= (y,a);
end
// the address has already been downgraded
m2c.deqReq;
endrule // (5) and (7)
5 Dn-req process, Dn resp send (cache)
7 Dn-req process, drop (cache)

## Slide 26: Child Voluntarily downgrades
Rules 1 to 8 are complete - cover all possibilities and cannot deadlock or violate cache invariants
rule startMiss(mshr == Ready);
let slot = findVictimSlot(state);
if(!isStateI(state[slot]))
begin // write-back (Evacuate)
let a = getAddr(state[slot]);
let d = (isStateM(state[slot])? dataArray[slot]: -);
state[slot] <= (I, _);
c2m.enq(<Resp, c->m, a, I, d>);
end
endrule // (8)
8 Voluntary Dn-resp (cache)

## Slide 27: Invariants for a CC-protocol design
Directory state is always a conservative estimate of a child’s state
  E.g., if directory thinks that a child cache is in S state then the cache has to be in either I or S state
For every request there is a corresponding response, though sometimes it is generated even before the request is processed
Communication system has to ensure that
  responses cannot be blocked by requests
  a request cannot overtake a response for the same address
At every merger point for requests, we will assume fair arbitration to avoid starvation