## Slide 1: Constructive Computer Architecture
Arvind
Electrical Engineering and Computer Science
Massachusetts Institute of Technology
6.1920: L01 – February 6, 2024

## Slide 2: 6.1920 Course Staff
Instructors
Sally Lee sally@csail.mit.edu
Thomas Bourgeat thomas.bourgeat@epfl.ch
Teaching Assistants
Admin
For most up-to-date information and handouts please consult Canvas
Martin Chan
martinch@mit.edu
Jianming Tong
jianming@csail.mit.edu
Tushar Krishna tushar@csail.mit.edu
Lab Assistants
Sanjay Seshan
seshan@mit.edu
Austin White
akwb@mit.edu
Arvind arvind@csail.mit.edu

## Slide 3: Computing Devices Then… EDSAC, University of Cambridge, UK, 1949
Notes: Fishbowl computing. Dramatic changes since then.

## Slide 4: Computing Devices Now
Dramatic progress in terms of size, speed, cost, reliability

## Slide 5: Computer architecture is about designing machines to meet some power, performance, cost and size constraints

## Slide 6: Studying Computer Architecture
A method of constructing machines: Machine descriptions which can be simulated in software and synthesized into hardware
Quantitative evaluation: To what extent designs meet various design criteria
Testing and verification: Does the machine do what it is supposed to do
This course is about “construction”

## Slide 7: The goals of this subject
Study computer architecture by constructing many different machines
Learn a new method of describing architectures where there is less emphasis on diagrams and more emphasis on executable descriptions
  Each architecture and each part of it would be defined as executable code in Bluespec System Verilog (BSV)
  Learning BSV is about learning a model of parallel programming (all hardware is parallel)
Learn about test benches, including designing your own
Learn about quantitative evaluation of designs

## Slide 8: BSV Design Flow
Bluespec Compiler
Xilinx Vivado
Simulator
Xilinx Vivado
Synthesis
Bluespec Simulator
Cycle Accurate
Design Compiler/ Encounter
BSV source
Verilog RTL
VCD output
Gates
Power Analysis
ASIC

## Slide 9
All the designs you do in this course can be implemented as ASICs without any changes in the source code. Time will not permit the class to explore ASICs but we will synthesis many designs and study resulting timing and area

## Slide 10: Course information
Every week, the class will have :
  Two lectures 9:30am-11:00am on Tues and Thurs
  One tutorial 3:30pm-5:00pm on Fridays
Lab assignments to be done individually. Each lab will provide ideas for the project
A project in the last two weeks to show and experiment with a cool architectural idea
Grade depends on Labs (70%) + Project (30%)
  A = >75%
  B = <75%
  C = <50%
  Late submissions get penalties, project is mandatory
No Quizzes

## Slide 11: Resources
BSV Reference manual
“Introduction to Digital Design as Cooperating Sequential Machines”, Arvind, Rishiyur S. Nikhil, James C. Hoe, Silvina Hanono Wachman, 2019
“Computer Architecture: A Constructive Approach”, Arvind, Rishiyur Nikhil, Joel Emer and Murali Vijayaraghavan, 2014 (read chapters 5, 6, 9, 10, 11 and 12 only; there may be inconsistencies with the lectures)
For most up-to-date information and handouts please consult Canvas

## Slide 12: Combinational circuits

## Slide 13: Combinational circuit
A combinational circuit is a pure function; given the same input, it produces the same output
It can be described using a Truth Table though it is not practical to do so for large number of inputs
  Size of truth table for a 32-bit adder?
We will use BSV to describe all circuits in this subject
a | b | c | s1 | s2
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0
f
a
b
c
s2
s1
232+32 rows

## Slide 14: Combinational Arithmetic-Logic Unit (ALU)
func
- Add, Sub, And, Or, ...
result
a
b
ALU
what does func look like?
function Data alu(Data a, Data b,
AluFunc func);
ALU performs all the arithmetic and logical functions
Each individual function can be described as a combinational circuit, and these can be combined together to produce a combinational ALU
Type of a, e.g., Bit#(32)
Notes: Data could be bit#(32)

## Slide 15: Types
A type is a grouping of values:
  Integer: 1, 2, 3, …
  Bool: True, False
  Bit: 0,1
  function Integer fname (Integer arg)
Every expression in a BSV program has a type; sometimes it is specified explicitly and sometimes it is deduced by the compiler
Thus, we say an expression has a type or belongs to a type
The type of each expression is unique

## Slide 16: User defined Types
Structures (t1 x t2 x …x tn)
typedef struct {
Word x_coord;
Word y_coord; // <- do not forget this ;
} MyStruct deriving (Eq, Bits, FShow);
Enumeration (tag1 + tag2 + … + tagn)
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu,
LShift, RShift, Sra} AluFunc deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT}
BrFunc deriving(Bits, Eq);
Type synonyms
typedef Bit#(8) Byte;
typedef Bit#(32) Word;

## Slide 17: Enumerated types
Suppose we have a variable c whose values can represent three different colors
  Declare the type of c to be Bit#(2) and adopt the convention that 00 represents Red, 01 Blue and 10 Green
A better way is to create a new type called Color:
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
BSV compiler automatically assigns a bit representation to the three colors and provides a function to test if the two colors are equal
Types prevent us from mixing colors with raw bits
Why is this way better?
If you do not use “deriving” then you will have to specify your own encoding and equality function

## Slide 18: Using an enumerated type: Combinational ALU
function Data alu(Data a, Data b, AluFunc func);
Data res = case(func)
Add : addN(a,b);
Sub : subN(a,b);
And : andN(a,b);
Or : orN(a,b);
Xor : xorN(a,b);
Nor : norN(a,b);
Slt : zeroExtend(pack(signedLT(a,b)));
Sltu : zeroExtend(pack(lt(a,b));
LShift: shiftLeft(a,b[4:0]);
RShift: shiftRight(a,b[4:0]);
Sra : signedShiftRight(a,b[4:0]);
endcase;
return res;
endfunction
Given an implementation of the primitive operations like addN, Shift, etc. the ALU can be implemented simply by introducing a mux controlled by func to select the appropriate circuit
Notes: Slt, Sltu?

## Slide 19: Using an enumerated type: Comparison operators
function Bool aluBr(Data a, Data b, BrFunc brFunc);
Bool brTaken = case(brFunc)
Eq : (a == b);
Neq : (a != b);
Le : signedLE(a,b);
Lt : signedLT(a,b);
Ge : signedGE(a,b);
Gt : signedGT(a,b);
AT : True;
NT : False;
endcase;
return brTaken;
endfunction
Notes: 19
We only compare with 0?

## Slide 20: Integer versus Bit#(32)
In mathematics integers are unbounded but in computer systems integers always have a fixed size
BSV allows us to express both types of integers, though unbounded integers are used only as a programming convenience
for(Integer i=0; i<32; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
integer

## Slide 21: Type declaration versus deduction
The programmer writes down types of some expressions in a program and the compiler deduces the types of the rest of expressions
If the type deduction cannot be performed or the type declarations are inconsistent, then the compiler complains
type error?
Type checking prevents lots of silly mistakes
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(2) ab = ha(a, b);
Bit#(2) abc = ha(ab[0], c_in);
Bit#(2) c_out = ab[1] | abc[1];
return {c_out, abc[0]};
endfunction

## Slide 22: Assigning to Bitvector elements
Means c is three bits wide and each element is set to zero
Element 0 of c is connected to 0 but the value of the rest of the elements is not affected
Initial value of a vector must be set; we use “?” if we don’t know the initial value
Bit#(3) c=0;
c[0] = 0;

## Slide 23: 2-bit Ripple-Carry Adder cascading full adders
add(x, y, c0):=
c[1], s[0] = fa(x[0], y[0], c[0]);
c[2], s[1] = fa(x[1], y[1], c[1]);
return {c[2],s};
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
Use fa as a black-box

## Slide 24: w-bit ripple carry adder
Tedious to write such repetitive equations
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
fa
x[w-1]
y[w-1]
s[w-1]
c[w]
c[w-1]
…
c[1], s[0] = fa(x[0], y[0], c[0]);
c[2], s[1] = fa(x[1], y[1], c[1]);
…
c[w], s[w-1] = fa(x[w-1], y[w-1], c[w-1]);

## Slide 25: Write a loop and unfold it using a compiler!
for(i=0; i<w; i=i+1)
c[i+1], s[i] = fa(x[i],y[i],c[i]);
return {c[w], s}
Can be done only when the value of w is known
c[1], s[0] = fa(x[0], y[0], c[0]);
c[2], s[1] = fa(x[1], y[1], c[1]);
…
c[w], s[w-1] = fa(x[w-1], y[w-1], c[w-1]);
“for” is *NOT* a loop like in python. It is just a shortcut to avoid having to write many lines. This fake loop has to be fully unrolled by the compiler.

## Slide 26: Combinational ALU
mux
a
func
…
Add
LShift
Eq
…
b

## Slide 27: Complex Combinational Circuits

## Slide 28: Multiplication by repeated addition
1101 (13)
1011 (11)
0000
x 1101
1101
+ 1101
+ 0000
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
mi = (a[i]==0)? 0 : b;
At each step we add either 1101 or 0 to the result depending upon a bit in the multiplier
We also shift the result by one position at every step
m0
m1
m2
m3
However, our addN circuit adds only two numbers at a time!

## Slide 29: Multiplication by repeated addition cont.
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
At each step we add either 1101 or 0 to the result depending upon a bit in the multiplier
We also shift the result by one position at every step
Notice, the first addition is unnecessary because it simply yields m0

## Slide 30: Multiplication by repeated addition ckt
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
add4
a1
m1
a2
m2
a3
m3
add4
add4
a0
m0
add4
0 0 0 0

## Slide 31: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Lot of gates!
This circuit uses 32 add32 circuits
Long chains of gates
  32-bit multiply has 32 ripple carry adders in sequence!
  32-bit ripple carry adder has a 32-long chain of gates
  Total delay ?
  2(n-1) FAs?
  2n FA delays, not nxn
Can we do better?
Stay tuned…
  why?
Notes: Iteration I produces the ith bit of answer using only i FAs. The most significant 32 bits are produced in the last step which involves an additional 32FA delays

## Slide 32: BSV Compiling phases
Type checking: Ensures that type of each expression can be determined uniquely; Otherwise, the program is rejected
Static elaboration: Compiler eliminates all constructs which have no direct hardware meaning
  Loops are unfolded
  Functions are in-lined; even recursive functions can be used as long as all the recursion can be gotten rid of at compile time
  After this stage, for example, the program does not contain any Integers because Integers are unbounded in BSV
Gates are generated (actually Verilog)

## Slide 33: Takeaway
Once we define a combinational ckt, we can use it repeatedly to build larger ckts
The BSV compiler, because of the type signatures of functions, prevents us from connecting them in obviously illegal ways
We can write parameterized ckts in BSV, for example an n-bit adder. Once n is specified, the correct ckt is automatically generated
Even though we use loop constructs and functions to express combinational ckts, all loops are unfolded, and functions are inlined during the compilation phase